## Slide 1: NOnA Accelerator Upgrades: Status
Phil Adamson
Fermilab
pa@fnal.gov
“It’s all fairly straightforward”
-- Jeff Hartnell this morning

## Slide 2: About this talk
This talk is not about the wonderful physics programme offered by the NOnA beamline
  NOnA
  MINERnA
  MINOS+
    See plenary talk by Jeff Hartnell this morning
Brief overview of current accelerator complex
Major upgrades required for NOnA
Status & schedule
This talk does not contain every detail of the upgrade project
  Please feel free to ask about your favourite subject

## Slide 3: Current NuMI operation
Linac: 750 keV – 400 MeV
Booster: 400 MeV – 8 GeV
Main Injector: 8 GeV – 120 GeV
Slip-stack 11 booster batches
2 batches to antiproton source
9 batches to NuMI
Cycle length is 2.2s
Typical peak NuMI beam power ~330 kW in mixed mode
Also SY120 fixed target program
Pbar storage in recycler
Pbar and protons to Tevatron
(plus BNB, MTA, NTF, …)

## Slide 4
NuMI neutrino beam
120 GeV protons
Focusing Horns
2 m
675 m
15 m
30 m
Target
Decay Pipe
π-
π+
νμ
νμ
Neutrino energy tuned by moving target (usually LE)
Change horn polarity to select νμ or νμ

## Slide 5: NOnA upgrades
Increase NuMI primary proton beam power
  330 (380) kW -> 700 kW
Additional focus on loss control
  Double the beam power
  Same tunnels
Change neutrino beam energy (focussing)
  Optimize flux at off-axis NOnA location

## Slide 6: Increasing beam power
Move slip-stacking to recycler
11 batch -> 12 batch
Increase Main Injector ramp rate (204 GeV/s -> 240 GeV/s)
330 (380) -> 700kW with only ~10% increase in per-pulse intensity
Main Injector
Recycler

## Slide 7: So need to rebuild recycler
Remove:
  Old transfer lines
    Small aperture (pbar: 6p/2p, protons: 15-20p)
  Stochastic cooling
  Electron cooling
    Pelletron
    Rebuild MI-30 with FODO lattice
  Various odds and ends that might be aperture restrictions
Add:
  New injection line from MI8 to recycler
  New RR->MI transfer line
  53 MHz RF system for slip-stacking
  Instrumentation
    BPMs
    Low-mass Ti multiwires
    IPMs
  Must maintain vacuum at 10-10 – 10-11 torr (TSPs)

## Slide 8: New MI-8 line
Switched dipole at 849
  ADCW (wide-gap modification of old ADC magnet)
Strontium Ferrite permanent magnet dipoles like rest of MI-8
Two Samarium Cobalt dipoles (space constraints)
Strontium Ferrite recycler quads, powered quad trims for lattice matching

## Slide 9: Installation in MI8
1-week shutdown in March 2011
  Electric company replacing switchgear offsite
Installed first PDD magnet in new MI8

## Slide 10: Rebuild 30 straight
New permanent quads for 30 straight in recycler
  Total cost cheaper than re-making existing quads
  ALARA

## Slide 11: 53 MHz RF in Recycler
Build 3 RF cavities
  A, B and hot spare
  150 kV per cavity
  Operating range: 52.809 MHz ± 1260 Hz
  10 KHz fast (~40 µs) phase shifters from Proton Driver
Recycle PAs and modulators from Tevatron
LLRF close to a copy of MI system

## Slide 12: 11 batches -> 12 batches
Currently place 81 bunches every 86 in MI
For NOnA, place 81 bunches every 84 in Recycler. (84 = 588/7)
Faster rising/falling edges -> many short kickers (6)
Already have 7 RKA magnets in MI: Gap Clearing Kicker system for loss control

## Slide 13: Gap Clearing Kicker System
6/7 magnets will move up to recycler for NOnA

## Slide 14: GCK measurements
Edges within specification
Slower edge in damper measurement might be artifact
Damper (beam) measurement
Calculated B from measured voltages
For recycler, building “tail bumper” to cancel tail
Tail measurement similar to electrical measurements (good)

## Slide 15
Green points: contact measurement at V105
GCK on for a week
Already as low as end of 2009 shutdown
GCK reducing local losses

## Slide 16: Increase MI ramp rate
2 new MI cavities to maintain bucket area
New transformer for vertical quad bus
Increased heat load on cooling ponds
  Will need more cooling for summer – study underway looking at future cooling needs (not just NOnA )
    More ponds?
    Run a chiller in summer?
    Shade ponds?

## Slide 17: Beamline upgrades
Increase rep rate
  2.2s (2.0s) -> 1.33s
Replace 5 3Q120 quads with ones from A150 beamline (better cooling)
Upgrade magnet power supplies
  Faster ramp
  BULB
    Better regulation
    Current monitor -> beam permit
New kicker power supply
Beam intensity doubled, but beam loss in water-bearing rock must not double
  New 1 mil Ti multiwires - lower mass in beam

## Slide 18: Off-axis neutrino beam
Off-axis, neutrino energy driven by angle
Adjust focusing to optimize flux
0
20

## Slide 19: Target Hall Upgrades
NOvA: new horn 1 (thinner o.c.)

## Slide 20: NOnA target
NuMI target (top) must fit inside horn 1
  Small, mechanically weak. Recent problems – failure of water cooling lines
NOnA target (right) upstream of horn 1 (neutrino energy from off-axis angle)
  Much more robust design. Water cooling 8 times further away from beam than NuMI
Target construction in progress – delivery this fall

## Slide 21: Target Carrier
“Prototype” carrier complete
  Expect to use as first production carrier
  Shown here with target/baffle mockup

## Slide 22: Schedule & Summary
Tevatron operation completes by October 1
Begin NOnA shutdown March 5 2012
  Shutdown scheduled for 11 months
  Current installation schedule has work completed in 8-9 months
    Then commission new accelerator complex
    If accelerator work done before NuMI, can get an early start on commissioning
NOnA accelerator upgrades proceed on schedule
I look forward to commissioning the new complex and swift progress towards 700 kW

## Slide 23: NOnA Accelerator Upgrades: Status
Phil Adamson
Fermilab
pa@fnal.gov

## Slide 24: Slip-stacking
Neutrino experiments want more beam!
Inject 11 batches rather than 6
  But pay for it with increased losses
  (<95% efficiency)

## Slide 25: Slip-stacking recapture (real data)

## Slide 26: Transfer and new MI8 lines
847
101
103
Recycler
8 Gev line
100
850
102
104
V2 (PDD) 19.2 mr
HBEND (35 mr)
VLAM (MLAW) 13.6 mr (DC)
K
HKICK (1.208 mr)
5 kickers 1 bumpers
848
MI8
849
852
851
103
102
MI
QR853
QR852
New Dipole Magnets
Mini-Boone switch magnet
846
New MQT trims
MQT trims
ADCW Switching
K
RR-30 straight section
307
MLA
RR extraction Kicker
MI-30 straight section
304
306
Q308
Q304
Q306
K
301
VUP1
VDN2
MI VLAM Rolled
Q302
GM229B
303
K
GM231A,B
GM232A,B
302
305
308
309
K
Q303
Q305
Q307
Q309
Q301
GM230A,B
Trim quads
Q805
Q804
Q803
Q802
Q801
MI injection Kicker
Mirror magnets