## Slide 1: Design, maintenance and operational aspects of the CNGS target
M. Calviani (CERN-EN/STI) on behalf of the CNGS Team
4th High Power Targetry Workshop
Malmö, Sweden, 2nd – 6th May 2, 2011

## Slide 2: Outline
Introduction to CNGS physics case and design guidelines
CNGS target design
  FLUKA simulation optimization
  Engineering design of the target and auxiliary equipment
Operational aspects of the installation: selected topics
  Maintenance of the target system
  Investigation on target motorization failure

## Slide 3: General layout of the CNGS installation
Air cooled graphite target magazine (p/K production)
2 horns (horn + reflector)  water cooled, pulsed with 10ms half-sine wave of 150/180 kA, 0.3 Hz, remote polarity change (focusing of charged mesons)
Decay pipe  1000m 2.45 m Ø, 1 mbar vacuum (decay in flight)
Hadron absorber  C core + Fe, ~100 kW absorption proton and other hadrons
2 muon monitor stations: m fluxes and profiles (direction of the n beam towards LNGS)

## Slide 4
SPS
North Area and Prevessin site
PS and Meyrin site
LHC
TI2 LHC injection
TI8 LHC injection
CNGS
Target area
Decay pipe
Hadron stop + muon pits
n towards LNGS
SPS: 2 fast extraction of 400 GeV/c protons every 6 seconds
Nominal 2x 2.4*1013 ppp in 10.5 ms interleaved by 50 ms (currently 2x 2.1*1013 ppp)
Beam power: ~500 kW (currently 448 kW)
Sigma = 0.53 mm
Ultimate 2x 3.5*1013 ppp

## Slide 5: Physics requirement for the CNGS beam
The energy spectrum of the nm is well matched to R~stCC/En2 at ~17 GeV to maximize the signal rate (nt appearance)
Low anti-nm and ne contamination
CNGS is a long base-line appearance experiment, designed for nmnt oscillation search  nt appearance in a (almost) pure nm beam
CNGS approved for 22.5*1019 POT (5 y with 4.5*1019 POT/y)
… up to now 10.5*1019 POT
Few nt expected in OPERA and ICARUS detectors
3.5 GeV (threshold for t production)

## Slide 6: Example of neutrino events in OPERA and ICARUS
ICARUS: 600 ton Liquid Argon TPC
High sensitivity and online reconstruction of tracks
OPERA: 1.2 kton emulsion target detector
146000 lead emulsion bricks
First nt detected
arXiv:1006.1623v1 8 June 2010

## Slide 7: CNGS description with FLUKA
The CNGS beam-line facility is fully described within the FLUKA Monte Carlo code for various purposes:
target
horn
reflector
He bags
TCC4
TSG4
Decay pipe
Optimization of the target design in the initial project stages
Energy deposition in the secondary beam line  mechanical and thermal analysis
Prompt and residual dose rate  radioprotection
Monitor beam response  commissioning and diagnostics (m distrib. at m-pits)
Predict neutrino beam energy spectrum/composition at LNGS

## Slide 8: Past experience at CERN
The design of the CNGS target takes advantage of the experience with previous fixed targets at CERN
Operational experience with the target (e.g. corrosion in humid/radioactive environment)
FLUKA used for beam simulations and comparison with n-induced CC events in NOMAD
WANF muon pits good agreement for the 3 detector regions
S. Peraire, 1996
 T9 WANF target (CHORUS and NOMAD experiments) (~180 kW beam)
 11 Be rods, 3 mm Ø, 10 cm long, spaced every 9 cm, He cooled (forced flow)
Notes: 2x 1.8E13 every 14.4 seconds

## Slide 9: Physics requirement of the CNGS target
Provide the highest possible proton interactions
Decrease probability of secondaries reinteraction
For HE n beams: target needs to be segmented, in order to allow small-angle high momentum secondaries to escape the target with less path length
Target need to be robust to resist beam-induced stresses
Due to particle energy deposition the target must be cooled
The target should not be cooled by water (avoid mechanical shocks and activation/radioprotection issues)
Material choices should minimize the absorbed beam power and maximize radiation resistance
Target should be replaceable, with in-situ spares
With the following technological constraints:

## Slide 10: Design optimization of the CNGS target
 Due to proton beam size and target configuration, the alignment of the beam line elements is not “too much” critical for CNGS neutrino fluxes
A thorough study was performed to optimize the physics and engineering of the target unit.
P. Sala (2001)
Effect of target configuration on p yield
Effect of beam s and target diameter of p yield
3mm comparison with WANF target
s=0.53 mm is the reference beam
Effect of beam displacement
Notes: A variety of alternatives for geometry, configuration and beam size were investigated!

## Slide 11: CNGS target rod configuration
Baseline configuration
5 mm Ø
Proton beam
90 mm
62 mm
508 mm
4 mm Ø
100 mm
Beam focal point
2 mm gap
Baseline target:
13 graphite rods, 10 cm each for a total of 3.3 lI
5 mm Ø for the first two (maintain a margin of security  containment of proton beam tails), 4 mm Ø for the others
The first 8 are separated by 9 cm each to better develop meson production, with the last 5 packed to reduce longitudinal smearing in p production (for a better focalization)
Chart: CNGS Peak Thermal Load
 | 75.6144 | 89.712 | 89.712 | 88.4304 | 79.4592 | 71.7696 | 64.08 | 57.672 | 47.4192 | 55.1088 | 57.672 | 56.3904 | 52.5456
 | 118.1475 | 140.175 | 140.175 | 138.1725 | 124.155 | 112.14 | 100.125 | 90.1125 | 74.0925 | 86.1075 | 90.1125 | 88.11 | 82.1025
Total power in rods!
Nominal (4.8*1013 p/6s cycle)  886 W
Ultimate (7.0*1013 p/6s cycle) 1292 kW
Not in scale

## Slide 12: The CNGS target unit
Target unit is conceived as a static sealed system filled with 0.5 bar of He (@cold)
Cooling of the target rods is made by radiation to the Al tube and convection
The target “revolver” is flushed with air which keeps the aluminum temperature <100 ˚C
Material used for the target
Tube: Al-Mg alloy
Windows: Beryllium
Target support: C-C
Target rod: fine-grain graphite
Upstream window (Be Ø1.5”)
Downstream window (Be, Ø4”)
Target support tube (C-C composite)
Target rods and support structure
Sealed cooling finned tube (Al 5083 H111)
Central tube
End cap
End cap
0.5 bar at room temperature, 1.0 bar at operating conditions

## Slide 13: Additional details on the target
The tube has annular fins to enhance the convective heat transfer
  He gas best to keep target wall at lower temperature BUT higher DT=76K
  Al anodized to increase radiative heat transport to the tube
Dedicated configuration conceived to limit the heat load on the target itself
Target rods are on a carbon support structure with holes in order to increase thermal exchange
Electron beam welding!
635 mm Ni-coated Be window (preserve from ambient corrosion) (381 mm upstream)
In order to reduce the amount of material (e.g. beam heating and thus mechanical stresses) the exit Be window is e-welded directly onto the Al alloy tube

## Slide 14: CNGS target rod configuration (current configuration)
Graphite target with baseline geometry under He (Graphite 2020PT by Carbone Lorraine)
  Best understood carbon (r=1.76 g/cm3)  standard target!
Carbon target with baseline geometry under He (Sintered Carbon SC24 by Sintec Keramik)
C-C composite target with baseline geometry under He (Aerolor A035 by Carbone Lorraine)
  C-C suited for operation at high temperature (thermal shock resistance and low coefficient of thermal expansion) But radiation damage?
C-C composite target with baseline geometry under vacuum (Aerolor A035 by Carbone Lorraine)
  Vacuum in order to address a possible concern of stress cycling on the Be window from thermal cycling of gas
“Safe” target: graphite target with all 5 mm diameter rods under He
  Introduced as a possibility to increase the beam size from 0.53 mm to 0.75 mm
All the materials from the different producers have been tested and analyzed in lab to cross-check the technical specifications
5 units installed in a single target magazine
Notes: Stresses on Be window downstream target: keeping the unit under vacuum rather than filling with inert gas. The gas heats up during beam on periods and then cools down during beam off which lead to repeated bending of windows, hampering the lifetime of Be windows  multiple solution for target

## Slide 15: The CNGS target units as built
5 units (1 active + 4 in-situ spare) are hosted in a target magazine
An additional spare magazine is available in case of complete target failure
C-C structural tube
Graphite rods
Al tube, anodized inside
Al external fins
Implementation in FLUKA
Tgraphite ~ 990 ˚C
TC-C ~ 375 ˚C
THe ~ 365 ˚C

## Slide 16: Target unit as built and installed in CNGS
Alignment table (movable)
Base table (fixed)
Target displacement mechanism (lifting jacks)
Target magazine
BPKG
Rotating disks
Rotation mechanism
Notes: The alignment table is supported by the alignment mechanism made of two vertical lifting jacks
supporting a horizontal linear guide at each end of the table. Jacks and linear guides are driven by four
motors fixed on the outer surface of the cast-iron passage-wall and hosted in recesses inside the marble-side
shielding. A “base table” resting on the target base shielding is placed underneath the alignment mechanism,
allowing its removal by the crane.

## Slide 17: The target base/alignment table
Fast coupling system
Indexing system
Finned internal shielding
Base/alignment table is placed by guiding grooves on three adjustable points
Motorization driving the alignment table is located outside of the shielding
The connection is realized through the shielding by shafts with fast coupling systems
Horizontal movement
Vertical movement
Supporting points of the alignment table
Notes: Each of the target, alignment and base tables are placed on 3 points (one fixed, one sliding and one free
support point) which allow pre-alignment and accurate positioning.

## Slide 18: Target assembly cooling
Two main air streams in the TS, not affected by each other (3600 m3/h cooling capacity):
Vertical airflow parallel to the fins of the target assembly  TARGET
  ~6 kW to evacuate (3.4 kW active unit + 1.5 kW spare unit)
Horizontal airflow parallel to the fins of the shielding  SHIELDING
  ~15 kW (~13 kW side wall shielding)
Proton beam
Target unit cooling
Target station cooling
Tav = 85 ˚C, Tmax = 93.5 ˚C (finned case!)
Tavshield ~40 ˚C, Tmaxshield ~300 ˚C
M. Kuhn (2005)
Notes: The presence of the fins increase the surface by 7x for the target and 10x for the shielding walls!

## Slide 19: Stresses on the CNGS target rods
A critical point for CNGS is the possibility to receive off-axis beam
Worst loading conditions (1.5 mm OA, ultimate intensity, cold target, no damping)
Stassi stress ratio (Stassi equivalent stress/tensile strength) employed for design consideration
Max. Stassi eq. stress found for 1.23 mm OA = 27.1 MPa
Time for equilibrium is > than bunch spacing  effect of the 1st bunch still present when the 2nd comes
32.4 MPa at 1.5 mm OA  Stassi ratio ~0.89
L. Massidda, CRS4, 2005, A. Bertarelli, CERN, 2003
Temperature increase & boundary conditions  dynamic stresses on the rods  rapid transversal vibration
Stassi ratio always lower than 0.7 (safety factor of 1.5!) for single bunch
Beam stability on target  well within these limits…
Notes: The Stassi stress criterion is adopted to evaluate the stress state in the structure and the Stassi ratio in particular. This design parameter is defined as the ratio betwee the Stassi equivalent stress and the tensile strength of the material

## Slide 20: DPA evaluation by FLUKA of the CNGS target rods
1 DPA
Operational T favors annealing and reduction of imperfection due to amorphous graphite
No apparent reduction in muon yield observed from 2008 to now (E. Gschwendtner, 2011)
Tests performed at BLIP (BNL) show no damage at 5.9*1020 POT in argon atmosphere of several type of graphite (P. Hurh, HB2010)
FLUKA adopted to evaluate the DPA on the target graphite material
~1.5 DPA for the first 3 rods assuming 10.5*1019 POT (~0.2 mm radius)
Expected ~3 DPA at the end of expected CNGS run
Shrinkage and reduction of thermal conductivity (higher stress)  minimized by operating at high T

## Slide 21: Structural limits of the CNGS target
Mechanical limits: dynamic (beam time structure) and static stresses (beam profile)
Thermal limits: determined by cooling system
Radiation damage: might lead to defects and target failures
M. Meddahi et al., CERN-AB-2007-013
Dynamic stresses  spreading the beam in more batches and increasing the spacing between extractions  up to 1*1014 p/cycle
At this stage, target cooling would be the limiting factor:
  Graphite erosion by sublimation (can be an issue from ~1.5 MW)
  Degradation of helicoflex seals
Nominal CNGS
4.8*1013 p/6s
1.38*1020 pot/y
7.6*1019 pot/y
4.56*1019 pot/y
Ultimate CNGS
7.0*1013 p/6s
~750 kW
~510 kW
RP limit
Secondary beam line elements (horn, HS, DP)
Design limit for target, kicker, instrumentation
CNGS working point
200d operation
200d operation, 55% efficiency
200d operation, 55% efficiency,
60% CNGS sharing

## Slide 22: Target rotation system failure – radiation induced effects on material
Usual yearly maintenance of the target unit includes(d):
Alignment motor maintenance, DC motors with torque limiter outside the shielding block  5 mm, precision of 100 mm
Rotation of the target magazines to 1) check the remote system movement capability and 2) to reduce formation of oxides in the bearings
During inspection/maintenance in March 2009 (@1.94*1019 POT):
Corrosion residues observed in the motorization elements (expected)
Increased torque in the magazine rotation motor (not expected!)
A thorough target inspection has been performed in April 2009
Fast coupling system
Motorization block

## Slide 23: Target in-situ inspection – April 2009
The target has been removed from the fixed shielding
Investigation of the rotating magazine via remote-controlled webcam-endoscopy
Downstream T40 target looking upstream
All the ball-bearings for target rotations have sign of rust
3 moves (with difficulties) when the barrel moves
1 (downstream) does not move at all
In-situ measured torque of ~30 N*m vs. a design value of 8 N*m

## Slide 24: Ball bearings irradiation in the CNGS target
Material for the original bearings:
Martensitic SS 440C (inner & outer races)
Martensitic SS X46Cr13 (balls)
Lubricant (YVAC3) and anti-dust cage used
New bearings ordered in 2009 from the original manufacturer without lubricant and anti-dust cage
 Installed in CNGS in July 2009 for irradiation on a specially designed bar
Top view
Lateral view
Notes: … the grades containing the lowest chromium, the highest carbon and sensitized, can be more rapidly attacked if a strong HNO3 environment develops

## Slide 25: 2010/2011 observations
End of 2009
2.7*1019 POT
~1.1 MGy
End of 2010
6.7*1019 POT (cum.), 2.7 MGy
Observations:
Significant rust/pitting corrosion present in both cases ???
Very difficult to turn the bearings, >>10 N*m estimated
Next steps:
Spare target with different ball bearings:
  Complete ceramic type – Si3Ni4 or ZrO2
  “Hybrid”, with ring in Cronidur 30/Alacrite 554 and spheres in Si3Ni4.
Testing of these bearings in CNGS (>June 2011)
If a target failure occurs:
Move manually (dose …)
Move with a motor
Risk of braking the coupling element
Exchange with spare target magazine
Low grade of X46Cr13 likely the cause of the observed failure (no alloying element, low Cr/high C content)
Notes: High carbon content in the 440C alloy might increase precipitation of carbides./
431C alloy: Cr 15-17%, C 0.20%, with Ni to improve corrosion resistance
440C alloy: Cr 16-18%, C 1.20% (high!)  possibility to precipitate carbides
Alacrite 554 (CoCr30W8)

## Slide 26: Conclusions
CNGS is in operation since 2006
  It has received up to now 10.5*1019 POT, out of the approved 22.5*1019 POT, performing very well (no target exchange needed)
The target design has drawn experience form past CERN fixed targets, with increased challenges due to the high proton beam power (510 kW  1.5 MW possible)
Operational issues encountered in operations are similar to those observed at other high power neutrino facilities
An upgrade of the spare target will be performed to prepare for a possible target failure

## Slide 27
Thanks a lot for your attention!

## Slide 28: Radiation on electronics issue (1/2)
CNGS installation is deep underground (~60 m below surface level)  no surface building above CNGS target area
A large fraction of electronic is located in the tunnel area
During CNGS run in 2007 (after 7.9*1017 pot)
Failure of ventilation system installed in the CNGS tunnel area due to radiation effects in the control electronics (COTS) (SEU due to high energy hadron fluence)
High-E (>20 MeV) hadron fluence for a nominal year
(107-109 HEH/cm2/y)
Ventilation unit control electronic in the service gallery
Operation stopped when a fluence of only 1-5*107 cm-2 was reached
L. Sarchiapone, A. Ferrari et al., 2008

## Slide 29: Radiation on electronics issue (2/2)
Modifications during 2007/2008 shutdown
Move as much electronics as possible out of the CNGS tunnel area
Create radiation safe area for electronics which needs to stay in the CNGS areas  massive shielding (movable plugs + chicane) added!
Accumulated dose not a problem for operation  HEH/nth effects on COTS electronics are a problem to be addresses since the beginning in the design of high power hadron machines!
2006/7 107-109 HEH/cm2/y
From 2008: <106 HEH/cm2/y
L. Sarchiapone, A. Ferrari et al., 2008

## Slide 30
Target
Horn + Reflector
SPS: 2 fast extraction of 400 GeV/c protons every 6 seconds
Nominal 2x 2.4*1013 ppp in 10.5 ms interleaved by 50 ms (currently 2x 2.2*1013 ppp)
Beam power: ~500 kW
Sigma = 0.53 mm
Ultimate 2x 3.5*1013 ppp

## Slide 31: FLUKA - accumulated yearly dose at target
~20 MGy/nominal year (upstream bearing)
~150 MGy/nominal year (downstream bearing)
Failure of the bearings become evident at ~60 MGy cumulated dose (1.94*1019 pot)
Test bearings are in a zone where the radiation is ~2 MGy/nominal year

## Slide 32: CNGS POT
Year | POT/yr
2006 | 0.08*1019
2007 | 0.08*1019
2008 | 1.78*1019
2009 | 3.52*1019
2010 | 4.04*1019
2011… | ~1*1019
Total | 10.5*1019
Nominal CNGS working point = 4.5*1019 POT/y
Received 10.5*1019 up to now
CNGS approved for 22.5*1019 POT
Before the CERN 1st LS (2013/14) CNGS would have accumulated ~18.9*1019 POT
Operation after this date will be addressed in 2012
Horizontal beam position [mm]
Vertical beam position [mm]
E. Gschwendtner, 2011
E. Gschwendtner, 2011
RMS=54 mm
RMS=77 mm
Beam on target position stability over the entire run (H/V)
 in agreement with the requirements of the design study (stresses on the target)

## Slide 33: Physics requirement of the CNGS target
Physics requirement from the CNGS target:
Provide the highest possible proton interactions
Decrease at the same time probabilities of secondaries reinteraction:
 For HE n beams the target needs to be segmented, in order to allow small-angle high momentum secondaries to escape the target with less path length
Physics optimization of the CNGS target
P. Sala (2001)
P. Sala (2001)
all 4 mm Ø
Overall length 2m, C length 1.261m “standard target in these figures”
Effect of target size (on p yield)
Effect of target configuration (on p yield)

## Slide 34: General design constrains – CNGS target
Target rods segmented and thin to maximize pion production and reduce secondaries reinteraction
Target need to be robust to resist beam-induced stresses
Due to particle energy deposition the target must be cooled
With the following technological constraints:
The target should not be cooled by water, in order to avoid mechanical shocks and increases activation/radioprotection issues
Material choices should minimize the absorbed beam power and maximize radiation resistance
Target should be replaceable, with in-situ spares
The target station should allow remote handling by a crane
The target station should allow remote calibration of the alignment table
L. Bruno

## Slide 35: Yearly accumulated dose – CNGS target
Transversal cut, end of target
K. Roeed, 2011
Dose below target along the beam direction
Transversal cut, beginning of target

## Slide 37
hBN collimator
Air inlet

## Slide 38
Proton beam
Flow separator