## Slide 1: SPIRAL 2 production station
Hanna Frånberg Delahaye
Radioactive beam production
GANIL-SPIRAL 2, Caen, France
May 3, 2011

## Slide 2: Lay out of the presentation
SPIRAL 2 phase 2
RNB production
Front end – production module
Neutron converter
Target and ion sources
Radiation levels in the production building

## Slide 3: The SPIRAL 2 construction
Figures
SPIRAL 2 phase 1
GANIL
DESIR
SPIRAL 2 phase 2

## Slide 4: Accelerator and beam line layouts
Diagnostics
Heavy ion source
d ion source
RFQ
LINAC
TIS unit
SPIRAL 2 phase 2 charge breeder
CIME
SPIRAL 2 phase 1 the accelerator
Experimental halls
SPIRAL 2 phase 2 radioactive ion beams
GANIL today

## Slide 5: SPIRAL2 goals
RI produced by fission process, fusion evaporation residues or transfer products
High intensity stable primary beams : P, D, 3,4He, heavy ions with A/Q=3 (1mA-5mA)
Energy range : from 2MeV/u up to 20MeV/u (D), 14.5MeV/u (HI), 33MeV (P)

## Slide 6: The construction has started

## Slide 7: The construction has started

## Slide 8: Production zones and 1+ beam lines
Maintenance area
Production area
Hot cell

## Slide 9: The hot cell
Deuteron beam
Maintenance area
Translation of roof and door
Beam transport area
Platform high voltage
8,2 m
21 m
7 m
9,4 m
Robot
Notes: All mounting and demounting will be performed in the maintenance cell
Test need to be perfomed to show the feasability.
Even though there are no tele operation availible in the first tests manual demounting and mounting is important so that sequences can be defined
Optimisation of the tools to optimise the equipement needed in the maintenance cell

## Slide 10: Size of the production module
Height: 2.15 m
Length: 3.20 m
Width: 2.20 m
Weigth: 8 t
Material: stainless steel 316L, Weight: 2,1t

## Slide 11: Components of the production module
Beam optics
Target and ion source
Neutron converter
Connectors easements
High voltage connectors
Pump module
Dismontable shielding
Dismontable shielding
Y. Huguet

## Slide 12: Overview of the production module
Converter door
Deuteron beam
Radioactif beam
Connector plate
Beam optics
Metal valves
High voltage connectors
HF
Converter connectors
Y. Huguet

## Slide 13: The hot cell
Deuteron beam
Maintenance area
Translation of roof and door
Beam transport area
Platform high voltage
8,2 m
21 m
7 m
9,4 m
Robot
Notes: All mounting and demounting will be performed in the maintenance cell
Test need to be perfomed to show the feasability.
Even though there are no tele operation availible in the first tests manual demounting and mounting is important so that sequences can be defined
Optimisation of the tools to optimise the equipement needed in the maintenance cell

## Slide 14: The front end

## Slide 15: Converter design
The 200 kW and 50 kW converter design
120 and 52 cm in diameter
rotation of 6-15 Hz (temperature difference 10-20°C/turn)
AXF-5Q from POCO Graphite inc
The working temperature of the graphite is1850°C
The d beam is stopped in the 7 mm graphite disk

## Slide 16: Converter design
Beam profile used for the thermo mechanical calculations
J. Bermudez, L. B. Tecchio, E. Udup
Material | Radiation damage [dpa] | Radiation source
Graphite | 50 | Deuteron beam
Wheel body (stainless steel) | 10-3 | Neutrons
Cooling panels (stainless steel) | 10-2 | Neutrons

## Slide 17: Prototype for the production of 14O at SP2
Length of the chamber (cm)
Emissivity of the walls
A tilted carbon target
chamber with black coating for thermal issues,
Cooling around the chamber
Beam stopper …
M G Saint Laurent et A. Pichard
3He
Ta window
MONOBOB
Target
Container
2300 K
P. Jardin, A. Pichard

## Slide 18: Beam scanning system
linear speed of 44 m/s is needed for a beam with a radius of 1 cm at 3 rms.
Centroïd of ± 3 cm give less than 150 W losses for a 35 kW beam
It implies a field of 350 G (due to 1/6 ions)
The preliminary frequencies are : 68.75 Hz for X and 60.5 Hz for Y.
Thermal simulations

## Slide 19: R&D on UCx targets
Study of physicochemical properties (by XRD, SEM, porosimeter etc.)
  Collaboration with the radiochemistry group
Study of release properties by irradiation tests
  Collaboration with the radiochemistry group and the nuclear physics group NESTER
Development of UCX targets throughout European collaborations:
  ActILab (ENSAR)
  Synthesis of UCX pellets
  Charactherisation
  Release tests
C. Lau

## Slide 20: UCx target
1300 UCx disks: Ø15mm/ th. 1 mm
Target : Ø=80 mm, l=80 mm
Cooled transfer tube with “zigzag”
Tantalum (Tungsten) oven

## Slide 21: Source ECR
Studies on the waveguide for the injection of the RF
Release times measurements connected to an oven.
Adaptation tests to a long extraction.
P. Jardin, A. Pichard

## Slide 22: Source Ionisation surface
One source for laser and surface ionisation
No mouvement of the point of extraction
P. Jardin

## Slide 23: Tests for the long extraction
Optimisation of the extractions of the production module and tests bench
228 µA with 99 % transmission
Feasible
O. Bajeat

## Slide 24: Resonant Ionization Laser Ion Source
N. Lecesne GANIL
GISELE ANR project: first prototype of the SPIRAL2 RILIS
(GANIL, IPNO)
TiSa System in collaboration with TRIUMF and the LARISSA group from Mainz University
Off line laser room fully equiped at GANIL
3 TiSa Cavities running
Up to 3.5W of InfraRed
beams produced
This work is supported by the French Research
National Agency (ANR) under contract
n° ANR-08-BLAN-0116-01

## Slide 25: Integrated doses from the n
<106 Gray / 3 months
105 Gray / 3 months
3·103 Gray / 3 months
2·105 Gray / 3 months
A. Savalle
Notes: Some words about the integrated doses. They are at the level of 10**6 gray for 3 months upper the module and 10**5 gray at the pumps, with an internal shielding inside the module. Outside the cocoon this dose is reduced with a factor of about 1 thousand

## Slide 26: Primary calculations of the Equivalent dose rates (EDR)
P_07
P_02
P_04
P_05
4 mSv/h
<1 mSv/h
1 mSv/h
4 mSv/h
7 mSv/h
A. Savalle
Notes: Now I present the results. In the horizontal plane the equivalent dose rates are between 1 and 7 micro-sieverts/hour, which is convenient (we have a blue zone).

## Slide 27: Primary calculations of the Equivalent dose rates (EDR) -2
Equivalent dose rates (EDR) -2
0,3 mSv/h
4 mSv/h
22 mSv/h
P_01
P_15
P_11
P_10
P_09
P_14
<7 mSv/h
50 mSv/h
20 mSv/h
> 10 mSv/h
A. Savalle
Notes: We see here the equivalent dose rates in different points around the production cell, whith the actual design of the building
In some places we are above the blue zone level and about at the green zone limit. Some additional shielding may be necessary.
Above the high energy transport line the level is too high and the access will be forbidden with the beam.

## Slide 28: Primary calculations of the Equivalent dose rates (EDR) -3
40 mSv/h
130 mSv/h
<7 mSv/h
A. Savalle
Notes: At the upper part of the cell, the concrete wall is not thick enough because of the crane. It has to be reinforced.

## Slide 29: Acknowledgements
O. Bajeat, J. Bermudez, C. Lau, Y. Huguet, P. Jardin, N. Lecesne,G. Normand, F. de Oliviera A. Pichard, M. G. Saint Laurent, A. Savalle, L. Serani, L. Tecchio, …

## Slide 30: SPIRAL 2 production module

## Slide 31: Beam parameters on target
Deutons
1/3 and 1/6 ion beams
Deutons 50 kW | R min (1rms) | Nominal radius (1rms) | R max (1rms)
x | 2.8 | 3.4 | 4
y | 3.1 | 3.4 | 
Deutons 200 kW | R min (1rms) | Nominal radius (1rms) | R max (1rms)
x | 6 | 7.1 | 8
y | 6.5 | 7.1 | 8.5
1/3 5 MeV/A | R min (1rms) | Nominal radius (1rms) | R max (1rms)
x | 1.9 | 2.2 | 2.7
y | 1.9 | 2.2 | 2.9
1/6 5 MeV/A | R min (1rms) | Nominal radius (1rms) | R max (1rms)
x | 1.9 | 2.2 | 2.8
y | 1.7 | 2.1 | 2.7
Matching LINAC/LHE
Achomatic deviation
2 sextuplets
Matching to the target
Beam scanning
system

## Slide 32: Ball bearings for the converter
Bearing Characteristic | WSP15312 RT4K4297 | W6001 RT4K4298 | W6002 RT4K4296
Material codification | W | W | W
Rings material | Stainless steel AFNOR X40CrMoVN16.2/ XD15NW |  | 
Hardness | 675 HV mini |  | 
Temperature of use | Max <500 |  | 
Balls material | Ceramic AFNOR Si3N4 |  | 
Hardness | 1050HV 10 mini |  | 
Cage Material | Stainless steel X105CrMo17/ AISI:440C |  | 
Lubricant | MoS2 Coating < 1 m |  | 
Holes | 40 mm | 12 mm | 15 mm
External Diameter | 68 mm | 28 mm | 32 mm
Number of balls | 20 (2x10) | 8 | 9
Nominal contact angle | 25° | 15° | 15°