## Slide 1: The European Spallation Source Neutrino Super Beam for CP Violation discovery
Marcos DRACOS
IPHC-IN2P3/CNRS Université de Strasbourg
August 14, 2015

## Slide 2: European Spallation Source
under construction phase
(~1.85 B€ facility)

## Slide 3: Having access to a powerful proton beam…
What can we do with:
5 MW power
2 GeV energy
14 Hz repetition rate
1015 protons/pulse
>2.7x1023 protons/year
p
π
ν
decay tunnel
proton beam
target
hadrons
hadronic collector
(focusing)
Detector
physics
⨂B
conventional neutrino (super) beam

## Slide 4: ESSνSB neutrino energy distribution
at 100 km from the target and per year (in absence of oscillations)
neutrinos
anti-neutrinos
almost pure νμ beam

## Slide 5: Can we go to the 2nd oscillation maximum using our proton beam?
Yes, if we place our far detector at around 500 km from the neutrino source.
MEMPHYS Cherenkov detector
(MEgaton Mass PHYSics studied by LAGUNA)
Neutrino Oscillations (Super Beam, Beta Beam)
Proton decay
Astroparticles
Understand the gravitational collapsing: galactic SN ν
  Supernovae "relics"
Solar Neutrinos
Atmospheric Neutrinos
500 kt fiducial volume (~20xSuperK)
Readout: ~240k 8” PMTs
30% optical coverage
(arXiv: hep-ex/0607026)

## Slide 6: Neutrino spectra
540 km (2 GeV)
below ντ production
neutrinos
anti-neutrinos
2 years
8 years
δCP=0

## Slide 7: 2nd Oscillation max. coverage
2nd oscillation max.
well covered by the ESS neutrino spectrum
1st oscillation max.

## Slide 8: Where to find all these protons?
European Spallation Source Linac

## Slide 9: ESS proton linac
The ESS will be a copious source of spallation neutrons
5 MW average beam power
125 MW peak power
14 Hz repetition rate (2.86 ms pulse duration, 1015 protons)
2.0 GeV protons (up to 3.5 GeV with linac upgrades)
>2.7x1023 p.o.t/year
Linac ready by 2023 (full power and energy)

## Slide 10: How to add a neutrino facility?
The neutron program must not be affected and if possible synergetic modifications
Linac modifications: double the rate (14 Hz → 28 Hz), from 4% duty cycle to 8%.
Accumulator (C~400 m) needed to compress to few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect)
  H- source (instead of protons)
  space charge problems to be solved
~300 MeV neutrinos
Target station (studied in EUROν)
Underground detector (studied in LAGUNA)
Short pulses (~μs) will also allow DAR experiments (as those proposed for SNS)
neutrino flux at 100 km (similar spectrum than for EU FP7 EUROν SPL SB)

## Slide 11: Previous Expertise
ESSνSB
BENE (2004-2008)
ISS (2005-2007)
EUROν (2008-2012)
LAGUNA (2008-2010)
LAGUNA-LBNO (2010-2014)
SNS (USA)

## Slide 12: Mitigation of high power effects (4-Target/Horn system for EUROnu Super Beam)
Packed bed canister in symmetrical transverse flow configuration (titanium alloy spheres)
Helium Flow
4-target/horn system to mitigate the high proton beam power (4 MW) and rate (50 Hz)
target inside the horn

## Slide 13: Energy Deposition from secondary particles, 3 horns, ESSνSB -1.6 MW/EUROnu -1.3 MW
Ptg = 212/104 kW
Ph = 52/32 kW
13.6/9.4 kW
3.5/2.4 kW
2.4/1.7 kW
2.1/1.2 kW
21/12.4 kW, t=10 mm
2.8/1.6 kW
target Ti=65%dTi , RTi=1.5 cm
6.3/3.4 kW, t=10 mm
Horn max
radial profile of power density kW/cm3
large increase of power (~x2) deposited on target @ ESS
FLUKA 2014, flair
(N. Vassilopoulos)
Notes: Large increase of power deposition on target compared to SPL

## Slide 14: General Layout of the target station (copied from EUROnu)
Split Proton Beam
Neutrino Beam Direction
Collimators
Horns and Targets
Decay Volume
(He, 4x4x25 m3)
Beam Dump
8 m concrete
Horn Support Module
Shield Blocks

## Slide 15: PSU
PSU: 8 times 4x44 kA modules
1-charger/capacitor/coil, 4-switches per 4x44 kA module
8 strip lines merged into 4 transmission lines in-out/horn
Large energy recuperation
a 4x44 kA module
x 8
Notes: Discharge 8 x 4x44kA modules to each horn every 20 ms, in between energy recovered at 97 % due to no-transformer situation

## Slide 16: Proton Beam Switchyard
Update of the switchyard preliminarily designed for EUROν with ESS beam parameters (config.1)
Parameter | EUROν | ESSνSB
Particle | H- | H-
Proton kinetic energy (GeV) | 4.5 | 2.5
Pulse intensity (mA) | 40 | 62.5
Avg beam power (MW) | 4 | 5
Beam rigidity (Tm) | 17.85 | 11.02
Macro-pulse length (linac) (ms) | 2.86 | 0.715
Pulse length (accu.) (μs) | 1.5 | 1.5
Pulse repetition rate (Hz) | 50 | 70
Other possible layouts currently being studied (i.e config.2)
config1.
config2.
Total length: 43.4 m
Max. B-field: 0.65 T (25 kA turns / pole)
Dipole length: 2 m
Total length: 72.2 m
Max. B-field: 0.73 T (29 kA turns / pole)
Dipole length: 2 m
• Selection criteria: number of magnetic elements needed + type of operation (i.e. simple or bi-polar) + prospective of beam dump requirements.

## Slide 17: Proton Beam Switchyard
> IPAC’15 Proceedings: E. Bouquerel, “Design Status of the ESSnuSB Switchyard”, MOPWA017
Quadrupole | Q1 | Q2 | Q3
Field gradient, T/m | 1.9 | -2.4 | 1.1
Intensity, NI per pole, kA | 30.8 | 39.0 | 17.8
Quadrupole | Q1 | Q2 | Q3 | Q4 | Q5 | Q6
Grad., T/m | 1.7 | -3.0 | 1.7 | 2.6 | -3.6 | 2.0
Intensity, NI / pole, kA | 27.2 | 48.3 | 28.5 | 41.8 | 59.9 | 33.7
• Assumptions:
- Norm. trans. Emittances: 225 μm (99.7%)
- Momentum dispersion: 0.1% rms.
config1.
config2.

## Slide 18: ESSνSB layout (adopted from EUROnu Super Beam, inspired by J-PARC (T2K))
Switching yard to four proton beams or accumulator rings
Iron (2.2 m) and concrete (3.7 m) shielding
Decay tunnel
He vessel (25 m)
PSU
Beam dump
Concrete surrounding shielding) (8 m)
Concrete surrounding shielding (8 m)
4-targets/horns
Vessel (He)
EUROnu
arXiv:1212.0732
Notes: Compact design to confine radiation

## Slide 19
Possible Layout
Courtesy T. Ekelöf, F. Gerigk
Avoid sharper bends

## Slide 20: Switch from 2.5 GeV linac
Assume again 0.15 T maximum B field
Consider switching dipoles as proposed for SPL-EURISOL
Switch for H-
(start of a quad package)
DRIFT 256.2 50 0
QUAD 410 4.61286 50 0 0 0 0 0
DRIFT 600 50 0
QUAD 410 -4.61286 50 0 0 0 0 0
DRIFT 256.2 50 0
(end of a quad package)
(start of the drift space)
DRIFT 1646.9 50 0
DRIFT 1646.9 50 0
DRIFT 1646.9 50 0
DRIFT 1646.9 50 0
(end of the drift space)
(start of a quad package)
DRIFT 256.2 50 0
QUAD 410 4.62783 50 0 0 0 0 0
DRIFT 600 50 0
QUAD 410 -4.62783 50 0 0 0 0 0
DRIFT 256.2 50 0
(end of a quad package)
(start of the drift space)
DRIFT 720.3 50 0
(end of the drift space)
(start of dipole)
BEND -4 25783.1 0 50 1
(end of dipole)
Drift-space between quads before dogleg ~ 6.6 m

## Slide 21: The ESSnuSB Accumulator
> IPAC’15 Proceedings: E. Wildner et al., “The Accumulator of the ESSnuSB for Neutrino Production”, THPF100
C=376 m
Straight Arc
J. Jonnerby, CERN
376 m long ring as one of the possible layout
Stripping foil injection: Temperature of the foils currently under studies
Summary of Lattice Parameters for the Accumulator
1797 K (H- Linac Beam)
H. Schönauer, CERN
T [˚K]
t [ms]
y [mm]
t [ms]
y [mm]
T [˚K]
T [˚K]
t [ms]
Maximum foil temperatures:
2050 K (H- + p circulating Beam)

## Slide 22: Possible locations for far detector
CERN
ESS
Kongsberg
Løkken
LAGUNA sites

## Slide 23: Which baseline?
Zinkgruvan
Garpenberg
Zinkgruvan is better for 2 GeV
Garpenberg is better for > 2.5 GeV
systematic errors: 5%/10% (signal/backg.)
CPV
MH
Zinkgruvan is better
atmospheric neutrinos are needed (at least at low energy)

## Slide 24: ESS Neutrino Super Beam DS
arXiv:1212.5048
arXiv:1309.7022
14 participating institutes from 10 different countries,
among them ESS and CERN

## Slide 25: Muon at the level of the beam dump
x (cm)
muons at the level of the beam dump
(per proton)
y (cm)
x (cm)
4.2x1020 μ/year
(16.3x1020 for 4 m2)
4.1x1020 μ/year
2.7x1023 p.o.t/year
muons/proton
<Eμ>~0.46 GeV
<Lμ>~2.9 km
10-3
input beam for future 6D m cooling experiments (for muon collider)
good to measure neutrino x-sections (νμ, νe) around 200-300 MeV (low energy nuSTORM)

## Slide 26: ESS Neutrino Super Beam Design Study
A H2020 Design Study has been submitted last September
  11 institutes (including ESS and CERN) from 8 European countries
  Decision:
    Overall score 13.5/15 (5/5 for Excellence)
    not enough to be funded (only 15 MEUR for this call)
    nevertheless, the evaluators recognise that ESSνSB answers one of the priorities defined in the European Strategy for Particle Physics.
New funding sources are now investigated in order to continue this design study (probably re-apply to H2020 2016/2017 call).
Some studies for H- injection and accumulation ring are included in an approved EU project concerning High Brightness neutron facility.

## Slide 27: ESS under construction
October 2014

## Slide 28: ESS Construction
February 2015
accumulator
target station
near detector
proton linac
First proton beam by 2019
Full power/energy by 2023

## Slide 29: ESS Construction
June 2015

## Slide 30: ESS Construction
June 2015

## Slide 31: Conclusion
Significantly better CPV sensitivity at the 2nd oscillation maximum.
The European Spallation Source Linac will be ready in less than 10 years (5 MW, 2 GeV proton beam by 2023)
Neutrino Super Beam based on ESS linac is very promising.
ESS will have enough protons to go to the 2nd oscillation maximum and increase its CPV sensitivity.
CPV: 5 σ could be reached over 60% of δCP range (ESSνSB) with large potentiality.
Large associated detectors have a rich astroparticle physics program.
Full complementarity with a long baseline experiment on the 1st oscillation maximum using another detection technique (LAr?).
A Design Study is urgently needed.

## Slide 32: Backup

## Slide 33: Neutrino Oscillations with "large" θ13
P(νμ→νe)
L/E
1st oscillation maximum
2nd oscillation maximum
θ13=1º
("small" θ13)
θ13=8.8º
("large" θ13)
for small θ13 1st oscillation maximum is better
for "large" θ13 1st oscillation maximum is dominated by atmospheric term
CP interference
CP interference
solar
solar
atmospheric
atmospheric
θ13=1º
θ13=8.8º
dCP=-90
dCP=0
dCP=+90
(arXiv:1110.4583)
more sensitivity at 2nd oscillation max.
L/E
L/E
L/E
1st oscillation max.: A=0.3sinδCP
2nd oscillation max.: A=0.75sinδCP
(see arXiv:1310.5992 and arXiv:0710.0554)

## Slide 34: DAR experiments (ESS/SNS)
Typical expected supernova neutrino spectrum for different flavours (solid lines) and SNS/ESS neutrino spectrum (dashed and dotted lines)

## Slide 35: Neutrino Oscillations with "large" θ13
(see arXiv:1310.5992 and arXiv:0710.0554)
2nd oscillation maximum is better
at the 1st oscillation max.: A=0.3sinδCP
at the 2nd oscillation max.: A=0.75sinδCP

## Slide 36: Systematic errors
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]

## Slide 37: Systematic errors and exposure
for ESSnuSB systematic errors see 1209.5973 [hep-ph] (lower limit "default" case, upper limit "optimistic" case)
P5 requirement: 75% at 3 σ
Neutrino Factory reach
10 years
20 years
(courtesy P. Coloma)
High potentiality

## Slide 38: Effect of the unknown MH on CPV performance
"default" case for systematics
small effect
practically no need to re-optimize when MH will be known
(P. Coloma)

## Slide 39: δCP accuracy performance (USA snowmass process, P. Coloma)
for systematic errors see (7.5%/15% for ESSnuSB):
Phys. Rev. D 87 (2013) 3, 033004 [arXiv:1209.5973 [hep-ph]]
arXiv:1310.4340 [hep-ex] Neutrino "snowmass" group conclusions
"default" column

## Slide 40: δCP coverage
CPV (2 GeV protons)
"nominal"
x2
after 10 years
with 2 times more statistics
systematic errors (nominal values): 5%/10% for signal/background
more than 50% δCP coverage using reasonable assumptions on systematic errors

## Slide 41: The MEMPHYS Detector (Proton decay)
(arXiv: hep-ex/0607026)

## Slide 42: The MEMPHYS Detector (Supernova explosion)
For 10 kpc: ~105 events
SUPERK
MEMPHYS
Diffuse Supernova Neutrinos
(10 years, 440 kt)