## Slide 1
Towards the simulation of proton beam induced pressure waves in liquid metal using the Multiple Pressure Variables (MPV) approach
Jana R. Fetzer, A. Class (May 21, 2014)

## Slide 2: Outline
Motivation
Multiple Pressure Variables Approach
Implementation in OpenFOAM
Validation
  Aero acoustic
  Liquid metal
Conclusion

## Slide 3: Motivation
outflow
inflow
nozzle
proton beam
European Spallation Source (ESS) proton beam key figures
  Proton beam power 5 MW
  Proton beam mean current 2 mA
  Long-pulse 2.86 ms
  Repetition rate 14 Hz
MEgawatt TArget: Lead bIsmuth Cooled
  Nozzle for flow conditioning and elimination of cavitation
  Successive beam pulses interact with fluid not subjected to the beam previously
  Pressure ~ 1bar
  Flow velocity 1.5-2 m/s
  LBE

## Slide 4: Motivation
expansion
volume
spoiler for
forced detachment
Dedicated design measures to counteract the effects of pressure waves
  Expansion chamber in Ubend
  Spoiler enforcing flow detacement
  Two internal free surfaces

## Slide 5: Motivation
Transient incompressible flow simulation
  Time step approx.:
Transient simulation resolving flow phenomena and acoustic phenomena
  Time step approx.:
- grid size
- flow velocity
- speed of sound
~ 1700 m/s (LBE)

## Slide 6: Multiple Pressure Variables Approach
Multiple Pressure Variables Approach
  Klein (1995) performed an asymptotic analysis using two spatial scales and one time scale to capture long wavelength phenomena
Basic non- dimensionalized variables
  , , , ,
  - global Mach number
Non-dimensionalized compressible Navier Stokes equations in primitive variables for the equation of state of a perfect gas

## Slide 7: Multiple Pressure Variables Approach
Asymptotic Considerations
  Vector of the primitive variables
    – local variable associated with convective phenomena
    – large scale coordinate associated with acoustic wave propagation
  Asymptotic expansion
Notes: Asymptotic expansion is inserted into the compressible Navier-Stokes Equations, terms multiplied by the same powers of the Mach number are collected to obtain a hierarchy of asymptotic limit equations.

## Slide 8: Asymptotic Limit Equations
Leading order continuity equation:
:
Leading, first and second order velocity equation:
:
Leading order pressure equation

## Slide 9: Interpretation of asymptotic equations
From the leading and first order velocity equation follows
Temporal evolution of from leading order pressure equation
  Integration with respect to over the domain
  Applying Gauß-Green theorem with – outward directed unit normal on the boundary of
compression
heat transfer

## Slide 10: Interpretation of asymptotic equations
Large scale average of second order velocity equation
First order pressure equation
Evolution equations for the large wavelength acoustics
“ - “ average over local structures

## Slide 11: Interpretation of asymptotic equations
Formal limit of asymptotic equations for in a bounded domain without heat conduction and global compression from the boundary
mathematical model of an incompressible flow with variable density

## Slide 12: Implementation in OpenFOAM
multi region solver
pisoMPVFoam
acoustic solver
velocity predictor
→ intermediate velocity field
pressure-velocity corrector
→ new
correct velocity
decompose pressure
thermodynamic pressure evolution
caclulate new pressure estimate p
map variables
solve acoustic system
Interpolate & mom
solve energy equation
calculate material properties f(T)
solve
solve
inner Iteration
outer Iteration

## Slide 13: Implementation of the MPV Method in OpenFOAM
Implementation is based on Munz et al. (2003)
  Pressure decomposition
    Thermodynamic pressure:
    Acoustic pressure
      constant on small spatial scale and varies on large scale
      Reference length hydrodynamic scale:
      Reference length acoustic scale:
    Hydrodynamic pressure
M=0.125

## Slide 14: Validation
Validation Matrix
 | M→0 Limit | Heat Transfer & material properties | Mach number independent behavior | Interaction flow - acoustic | turbulence
cavity | x |  |  |  | 
cavity heated | x | x |  |  | 
pressure pulse propagation |  |  | x |  | 
vortex box |  |  | x | x | 
co-rotating vortex pair |  |  | x | x | 
backwards facing step | x |  |  |  | x
heated rod | x | x |  |  | x
… |  |  |  |  | 
target | x | x |  | x | x
aero acoustic
liquid metal

## Slide 15: Test Cases – Aero acoustic
Lid Driven Cavity
  Laminar, Re=1000
  M = 0
  Mesh: 129 x 129 nodes
Stream tracer visualization

## Slide 16: Test Cases – Aero acoustic
Horizontal and vertical velocity along vertical/horizontal cross-section
  pisoFoam and benchmark (Ghia et al.) comparison
Vertical velocity at horizontal cross-section
Horizontal velocity at vertical cross-section

## Slide 17: Test Cases – Aero acoustic
„Vortex in a box“ – generation of acoustic waves due to a rotating vortex
  Initial Conditions
  Mesh:
    Hydrodynamic 32x32 cells
    Acoustic 4x4 cells
slip
Initial density distribution

## Slide 18: Test Cases – Aero acoustic

## Slide 19: Test Cases – Aero acoustic
Generation of Acoustic waves by „Co-rotating vortex pair“
  Initial conditions
    p=1 bar
    M = 0.095
  Mesh
    Hydrodynamic: 100 000 cells
    Acoustic: 5184 cells

## Slide 20: Test Cases – Aero acoustic
t =0.9 s
t = 1.2 s
t = 1.5 s
t = 1.8 s
t = 2.1 s
Vortex merging

## Slide 21: Test cases liquid metal
Backwards facing step
  Inlet velocity 10 m/s
  k-ε turbulence model
  LBE @ T=450K
Inlet ux =10 m/s
no slip
x-velocity component at x = 0.2m vertical cut
x = 0.2m

## Slide 22: Conclusion & Outlook
MPV approach proposed for simulation of pulse-induced pressure wave/ hydrodynamics interaction
Low extra numerical effort for solving acoustics
Suitable for design optimization
Implementation based on OpenFOAM architecture (pisoFoam)
Extensive ongoing validation
Design measures to limit effects of pressure waves in META:LIC target will be analyzed
Input on experimental data on pressure waves is appreciated for validation

## Slide 23: References
R. Klein, „Semi-implicit extension of a Godunov-type scheme based on low Mach number asymptotics I: One dimensional flow“ Journal of Computational Physics, 121, p 213-237, 1995
C.-D. Munz, S. Roller, R. Klein, K.J. Geratz, „The extension of incompressible flow solvers to the weakly compressible regime“ Journal of Computers and Fluids, 32 (2003) 173-196