## Slide 1: Buncher Schematics & CAD Model based on MICE Cavities Alan Grant Daresbury (May 8, 2012)

## Slide 2: Muon Front End Cooling
Cooling section consists of 100 cells 0.75m in length
Total section length 75m
100 normal conducting RF cavities and 100 superconducting coils
Cavities RF frequency 201.25 MHz, gradient 15 MV/m.
Cavity length 0.5m, Coil length 0.15m
Two Cells
Be coated

## Slide 3: Cooling Section CAD Model
Cell length 0.86m NOT 0.75m. This is for vacuum vessels.
Cavity module maintained at 0.5m as schematic.
Coupling coil cross section as schematic .15m x .15m
Bellows required between each cavity / coil module.

## Slide 4: MICE RFCC Module Overview
RF Cavities
Coupling Coil
Tuner arms
Couplers