## Slide 1: DPA and Gas Production from Protons on W and Be
Brian Hartsell
FNAL
Feb 28, 2015

## Slide 2: DPA and Gas Production in Tungsten
Ran the Mu2e target in MARS15 using the following parameters:
  8 GeV protons on Tungsten target
  Gaussian distribution with 1mm X and Y sigma
  6mm diameter, 160mm length target
  3 bins/sigma radially, 1cm bins axially

## Slide 3: Results
Peak DPA:
  1.4e-18 DPA/p
Gas production:
  H: 60 appm/DPA
  He: 20 appm/DPA
Notes: Peak DPA occurs in first 2 cm

## Slide 4: Converted to yearly..
1.9e20 p/yr estimated
Peak DPA:
  260 DPA/yr
Gas production:
  H: 16000 appm/yr
  He: 5300 appm/yr
Notes: Peak DPA occurs in first 2 cm

## Slide 5: DPA and Gas Production in Beryllium
Ran an arbitrary case in MARS15:
  Varying energy protons on Beryllium target
    2 MeV, 250 MeV, 120 GeV
  Gaussian distribution with 0.3mm X and Y sigma
  2.1mm diameter (7 sigma), 10mm length target
  1 bin/sigma radially, 1cm bins axially

## Slide 6: Results
 |  | DPA | H | He
 |  | (/p) | (appm/DPA) | (appm/DPA)
120 GeV |  | 3.66E-21 | 1030 | 2885
250 MeV |  | 6.29E-21 | 720 | 3400
2 MeV | First 20um | 4E-19 | 10-30 | 0
 | Bragg Peak | 7.5E-18 |  | 
Values are shown averaged over a volume of:
  1 sigma diameter
  1cm depth for 120 GeV and 250 MeV, depth shown for 2 MeV

## Slide 7: Results scaled to LBNE style beam
 | DPA | H | He
 | (/yr) | (appm/yr) | (appm/yr)
120 GeV | 0.23 | 235 | 659
250 MeV | 0.39 | 283 | 1330
700kW case:
  1.3mm beam sigmas
  3.7E13 protons/sec
  100% uptime

## Slide 8: Acknowledgements
Many thanks to Nikolai Mokhov for his input and support for the MARS runs.