## Slide 1: The 325 MHz Solution
David Neuffer
Fermilab
January 15, 2013

## Slide 2: Outline
Front End for the IDS Neutrino Factory
  Basis for engineering/costs
    Rf, requirements
    Engineering required
  Redesign for 325 MHz
    ??
rf gradient/ B concerns
  Transit Time Factor
  Pill-box radius

## Slide 3: Front End rf
μCol-νFact Front End was matched to 201.25 MHz
  matched to Fermilab Linac
  Cooling at 200, 400, 600, 800 …MHz
Project X is matched to 1300 MHz (ILC)
  match to 650 /325/ 162.5…
    433, 216.67, …
  match to 162.5 or 216.7 is similar to 201.25
Match to 325 MHz is not as straightforward
  requires ~500  325 MHz rf in Buncher /Rotator
  apertures are more restricted

## Slide 4: IDS Baseline Buncher and φ-E Rotator
Drift (π→μ)
“Adiabatically” bunch beam first (weak 320 to 232 MHz rf)
Φ-E rotate bunches – align bunches to ~equal energies
  232 to 202 MHz, 12MV/m
Cool beam 201.25MHz
18.9 m
~60.7 m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
42 m
~80 m
p
π→μ

## Slide 5: Rf Buncher/Rotator/Cooler requirements
Buncher
  37 cavities (13 frequencies)
  13 power supplies (~1—3MW)
RF Rotator
  56 cavities (15 frequencies)
  12 MV/m, 0.5m
  ~2.5MW (peak power) per cavity
Cooling System – 201.25 MHz
  100 0.5m cavities (75m cooler), 15MV/m
  ~4MW /cavity – most expensive item
Front End section | Length | #rf cavities | frequencies | # of freq. | rf gradient | rf peak power requirements
Buncher | 33m | 37 | 319.6 to 233.6 | 13 | 4 to 8 | ~1 to 3.5 MW/freq.
Rotator | 42m | 56 | 230.2 to 202.3 | 15 | 12.5 | ~2.5MW/cavity
Cooler | 75m | 100 | 201.25MHz | 1 | 16 MV/m | ~4MW/cavity
Total | ~240m | 193 |  | 29 | ~1000MV | ~550MW 400MW from cooling

## Slide 6: rf constraints
Transit time factor
  T = 0.8 (200MHz,0.5m)
  0.52 (325MHz,0.5m)
  0.21 (450 MHz,0.5m)
  0.75(450 MHz,0.25m)
    must use shorter rf cavities
Pillbox radius:
  r0= 0.38 m at 300 MHz
  r0= 0.255 m at 450 MHz
g =0.50m
g =0.25m
J0(2.405x)

## Slide 7: Components of 325MHz System
Drift
  20T 2T
Buncher
  Po=250MeV/c
  PN=154 MeV/c; N=12
  Vrf : 0 15 MV/m
    (2/3 occupied)
  fRF : 550 371MHz
Rotator
  Vrf : 20MV/m
    (2/3 occupied)
  fRF : 370 326MHz
  N=12.05
  P0, PN245 MeV/c
Cooler
  325 MHz
  25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 8: Propagation through the transport
Z=1m
Z=58m
Z=78m
Z=104m
Z=151m
-20m
-40m
0.8 GeV/c
0.0 GeV/c
0.8 GeV/c
0.8 GeV/c
0.0 GeV/c
0.0 GeV/c

## Slide 9: Variant 325MHz System
Drift
  20T 2T
Buncher
  Po=250MeV/c
  PN=154 MeV/c; N=12
  Vrf : 0 15 MV/m
    (2/3 occupied)
  fRF : 490 365MHz
Rotator
  Vrf : 20MV/m
    (2/3 occupied)
  fRF : 364 326MHz
  N=12.045
  P0, PN245 MeV/c
Cooler
  325 MHz
  25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 10: Simulation Results
N :0.15<P<0.35 MeV/c
N: εT<0.03; AL<0.2
N: εT<0.015; AL<0.2
Simulation obtains
  ~0.125 μ/p within acceptances
  with ~60m Cooler
  shorter than baseline
But
  uses higher gradient
  325 MHz – less power

## Slide 11: Variations
Gradient is a bit higher than IDS baseline or initial Muon Collider version
  15/20/25 MV/m  0.125 μ/p
  12.5/18/22.5  0.115
  12/16/20 MV/m  0.102
  12/15/18 MV/m  0.095
Apertures are smaller
  Use higher field transport to make beam smaller?
  2T  3T ? (with stronger focusing making the beam smaller
    first try had similar to baseline (not much better…)

## Slide 12: Summary
325 Mhz Front End Possible
  similar capture to baseline
  shorter system
Needs higher gradient rf and a bit stronger transverse focusing

## Slide 13: Answers to Questions