## Slide 1: Neutrino Factory Front End (IDS) and Variations
David Neuffer
G. Prior, C. Rogers, P. Snopok, C. Yoshikawa, …
August 2011
NuFACT99 -Lyon

## Slide 2: Outline
Front End for the IDS Neutrino Factory
  baseline design for IDS
    Developed from study 2A, ISS
  Basis for engineering/costs
    Rf requirements
Variations
  rf gradient/ B concerns
    alternatives
      gas-filled rf/insulated rf/low-B/
  Losses – control
    Chicane, proton absorber
μ+-μ- Collider Front End
  Shorter bunch train
    Larger V’, rebunching
  Rebuncher
    Time reverse front-end

## Slide 3: IDS Baseline Buncher and φ-E Rotator
Drift (π→μ)
“Adiabatically” bunch beam first (weak 320 to 232 MHz rf)
Φ-E rotate bunches – align bunches to ~equal energies
  232 to 202 MHz, 12MV/m
Cool beam 201.25MHz
18.9 m
~60.7 m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
42 m
~80 m
p
π→μ

## Slide 4: Neutrino Factory Front End
23 bunches
0m
Drift - 80m
Bunch-110m
Rotate-155m
Cool-240m
700 MeV/c
0 MeV/c
-30m
30m
v
Drift from target ~80m
  Beam lengthens
Buncher (~33m)
  N=10
  P0=233MeV/c, PN=154MeV/c
  330 → 235 MHz
  V’= 0→9 MV/m
Rotator (~42m)
  N=10.05 –
    accelerate/decelerate bunches
  235 → 202 MHz,V’= 12 MV/m
Cooler (~80m)
  201.25 MHz, ASOL lattice
  15MV/m in rf cavities
  LiH or H2 cooling
Captures both μ+ and μ-
Δ=10λrf
Δ=10.05λrf

## Slide 5: ICOOL - G4beamline
P. Snopok has run the IDS front end with both ICOOL & G4 beamline
  High statistics (>105 tracks)
  Obtains ~0.1 μ+ and μ- /8 GeV p within acceptances
    εT < 0.03, εL < 0.15
Validation of simulation codes
  Simultaneous simulation of both signs

## Slide 6: Parameters of IDR baseline
Initial drift from target to buncher is 79.6m
  18.9m (adiabatic ~20T to ~1.5T solenoid)
  60.7m (1.5T solenoid)
Buncher rf – 33m
  320  232 MHz
  0  9 MV/m (2/3 occupancy)
  B=1.5T
Rotator rf -42m
  232  202 MHz
  12 MV/m (2/3 occupancy)
  B=1.5T
Cooler (50 to 90m)
  ASOL lattice, P0 = 232MeV/c,
  Baseline has 15MV/m, 2 1.1 cm LiH absorbers /cell

## Slide 7: IDS : hardware specification
Specify front end in specific rf cavities, frequencies
Buncher – 13 rf frequencies
  319.63, 305.56, 293.93, 285.46, 278.59, 272.05, 265.80, 259.83, 254.13, 248.67, 243.44, 238.42, 233.61 (13 f)
  ~100MV total
    Keep V’ < ~7.5MV/m
Rotator – 15 rf frequencies
  230.19, 226.13, 222.59, 219.48, 216.76, 214.37,212.28, 210.46,208.64, 206.90, 205.49,204.25, 203.26, 202.63,202.33 (15 f)
  336MV total, 56 rf cavities
    12MV/m at 2/3 occupancy
Cooler
  201.25MHz –up to 75m ~750MV
    ~15 MV/m, 100 rf cavities
Magnet Requirements:

## Slide 8: Rf Buncher/Rotator/Cooler requirements
Buncher
  37 cavities (13 frequencies)
  13 power supplies (~1—3MW)
RF Rotator
  56 cavities (15 frequencies)
  12 MV/m, 0.5m
  ~2.5MW (peak power) per cavity
Cooling System – 201.25 MHz
  100 0.5m cavities (75m cooler), 15MV/m
  ~4MW /cavity
Front End section | Length | #rf cavities | frequencies | # of freq. | rf gradient | rf peak power requirements
Buncher | 33m | 37 | 319.6 to 233.6 | 13 | 4 to 7.5 | ~1 to 3.5 MW/freq.
Rotator | 42m | 56 | 230.2 to 202.3 | 15 | 12 | ~2.5MW/cavity
Cooler | 75m | 100 | 201.25MHz | 1 | 15 MV/m | ~4MW/cavity
Total drift) | ~240m | 193 |  | 29 | ~1000MV | ~550MW

## Slide 9: How Long a Bunch Train for IDS?
ISS study alotted space for 80 bunches (120m long train)
For IDS 80m (54 bunches) is probably plenty
100
~60m
~80m
Study ISS
120m
80m
ISS
IDS
n
Muon Decays
IDS: ~3 bunch trains simultaneously
-both μ+ and μ-

## Slide 10: Possible rf cavity limitations
V’rf may be limited in B-fields
  800 MHz pillbox cavity
  200 MHz pillbox test (different B)
NF needs up to ~1.5T, 12 MV/m
    More for cooling
Potential strategies:
Use Be Cavities (Palmer)
Use lower fields (V’, B)
  <10MV/m at 1.5T?
  Need variant for cooling ?
Cooling channel variants
  Use gas-filled rf cavities
  Insulated rf cavities
  Bucked coils (Alekou)
  Magnetic shielding
201MHz
805MHz
Need More Experiments !

## Slide 11: Cooling Lattice variations
Gas-filled rf
  With LiH absorbers
Magnetically shielded
  Small B at rf
Magnetically Insulated
  B  rf surface
Bucked Coil
  Reduced B in rf
  Alekou

## Slide 12: Problem: Beam losses along Front End
Start with 4MW protons
  End with ~50kW μ+ + μ-
    plus p, e, π, …
    ~20W/m μ-decay
  ~0.5MW losses along transport
    >0.1MW at z>50m
Want “Hands-on” maintenance
  hadronic losses < 1W/m
  Booster, PSR criteria
  Simulation has >~100W/m
    With no collimation, shielding, absorber strategy
Drift
Cool

## Slide 13: Control of Front End Losses
Add shielding
  Resulting losses ?
Chicane and proton absorber to localize losses (C. Rogers)
  Removes most protons
  Most desired μ’s survive
  Greatly reduces downstream activation problem
Shielding ?
12.7 m
~60.0 m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
42 m
~90 m
p
π→μ

## Slide 14: Muon Collider/NF Beam Preparation
Baseline Muon Collider beam preparation system identical to that for Neutrino Factory
  downstream portions (6D cooling, acceleration, collider) are distinct
    much more cooling and acceleration needed for collider
Neutrino Factory
Muon Collider

## Slide 15: Front End for Muon Collider
Muon Collider front end is different
  must capture μ+ and μ-
  want single bunches (not trains)
    Bunches are recombined …
  Maximum μ/bunch wanted
  Longitudinal cooling needed;
  Larger rf gradient can be used (?)
    NF will debug gradient limits
    Cost is less constrained
Use shorter BR system, more gradient, and capture at higher momentum
  230  270 MeV/c
  150m  120m
  9/12/15 MV/m  15/16/18 or 15/18/20 MV/m
  1.5T2T

## Slide 16: Muon Collider variants
ΔN: 108
Rf gradients: 12.5  15  18 MV/m
  Or 15  18  20 MV/m
Shorter system ~102m
14.05 m
~33m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~25.5m
27 m
~80 m
p
π→μ

## Slide 17: Variant front ends for muon collider
Front end Scenario | Drift, Buncher, Rotator Length | Rf Voltages | Full length (w 75m cooling) | +/p (t<0.03, L<0.3m) | -/p (t<0.03, L<0.3m) | Core bunches, NB, all -/p
IDS/NF | 80.6, 33, 42m | 09, 12, 15 | 230m | 0.086 | 0.116 | 20/0.107
N=10 | 55.3, 31.5, 33 | 012, 15, 18 | 205 | 0.106 | 0.143 | 16/0.141
N=8 | 47.8, 35.5, 27 m | 015, 18, 20 | 180 | 0.102 | 0.136 | 13/0.123
Table 1: Comparison of muon source front end systems.

## Slide 18: Integrate into 6-D cooling system
Initial Cooling transition
  NF transverse cooling only
  Transition to 6-D cooling needed
    Snake ? HCC? “Guggenheim”?
    Split μ+- μ-
    Cool 6-D by large factors
Recombine Bunches
    After cooling to small bunches
  Front end splits 1 huge emittance bunch into string of smaller ε –bunches
    Can we time reverse to combine cooled bunched to single bunches ?

## Slide 19: Bunch Recombination: Helical Channel
Would like a large dependence of path length on energy
Helical channel naturally has that
  Linear dependence is nicest …
η=0.43 looks possible
  HC – B= 4.2T bd=0.75, bq=0.4
  κ=1, λ=1.6m, P0=290MeV/c
  Dˆ=1.7, D=0.44m
    “γt”=1.085

## Slide 20: Longitudinal Dynamics in Helical Channel
Set up an HCC & see if bunch recombination is possible
  κ=1, η=0.43
    λ=1m
Very linear bunching over T=150—280 MeV
See if one can set up HC line for rebunching with this case
  Defer matching problem by using constant HCC

## Slide 21: Simulate in 3-D- G4BL –C Yoshikawa
Obtain beam from end of 3-stage HCC channel - K. Yonehara
  13 bunches, εL =0.0011m
  η=0.43 transport
40m 1MV/m rf
  204  270 MHz
    (+45° to -45° ) (N=12.25)
    η=0.43
60m drift
200MHz rf -10MV/m
  >95% capture
  εL = ~0.040
60MeV
60ns
z = 0 m
z = 40 m
z = 100 m
z = 105m

## Slide 22: Summary
Muon Collider:
  Need to integrate bunch combiner into complete cooling scenario
ν-Factory front end
  costing exercise for IDR
    “Most Likely” cost range?
  rf in magnetic fields ?
    adapt to rf measurements
  manage losses
    chicane/absorber/…
    simulation studies

## Slide 23: Questions?