## Slide 1: Bunch trains for Neutrino factory/ Collider
David Neuffer
November 2013

## Slide 2: Outline
Front End
“Muon Collider” versions
325 MHz
Add Chicane/Absorber
  rematch

## Slide 3: Fermilab PIP X 4
Linac, Accumulator, Compressor run at 15 Hz – 4 bunches
  bunches at 60 Hz
    4 bunches
  1 bunch at time into neutrino factory
    1 + and 1 - batch per cycle
    60 Hz neutrino factory
  Without trombone
    60 Hz single p bunch for collider
  With trombone
    41 15 Hz bunches for collider

## Slide 4: 325MHz System “Collider”
Drift
  20T 2T
Buncher
  Po=250MeV/c
  PN=154 MeV/c; N=10
  Vrf : 0 15 MV/m
    (2/3 occupied)
  fRF : 490 365MHz
Rotator
  Vrf : 20MV/m
    (2/3 occupied)
  fRF : 364 326MHz
  N=12.045
  P0, PN245 MeV/c
Cooler
  245 MeV/c
  325 MHz
  25 MV/m
  2 1.5 cm LiH absorbers
  /0.75m

## Slide 5: Simulation Results
N :0.15<P<0.35 GeV/c
N: εT<0.03; AL<0.2
N: εT<0.015; AL<0.2
Simulation obtains
  ~0.125 μ/p within acceptances
  with ~60m Cooler
  shorter than baseline NF
But
  uses higher gradient
  shorter than baseline NF
  325 MHz – less power
  more bunches in bunch train
Useful
cooling

## Slide 6: 325 Collider w/Updated Chicane/Absorber
13m chicane
  *6.5m  +21.67°,-21.67º
    particle 1-283 MeV/c
    particle 2-194 MeV/c
  Add 30m drift before absorber
absorber at ~65m
    10cm Be
    particle 1-250 MeV/c
    particle 2-154 MeV/c
  Bunch (N=12) 015 MV/m :496 365 MHz
  Rotate (N=12.045 )– 20MV/m : 365326.5MHz
  Cool -325MHz -25 MV/m
    pref=245 MeV/c
p
14.75 m
~20.5m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~21m
24 m
~80 m
π μ
6.5+13m chicane
+30.1 m drift
0.1 m Be
Chicane
SREGION ! bentsol
6.0 1 1e-2
1 0. 1.0
BSOL
1 2.0 0.0 1 0.283 0.0 0.058181 0.0 0.0 0.0 0. 0. 0. 0. 0.
VAC
NONE
0. 0. 0. 0. 0. 0. 0. 0. 0. 0.

## Slide 7: ICOOL results
325 “muon collider” with chicane absorber
  with added drifts between chicane and absorber
    ~30m
  ~0.12 μ/p  ~0.1 μ/p
  smaller emittance beams
    scraped to better fit
All μ+ (0.15<pμ <0.35)
μ+ (A <0.03, AL <0.2)

## Slide 8: 325 (w chicane/absorber)
1.0 GeV/c
0.0 GeV/c
~60 m long bunch train
  ~60 325 MHz buckets
For collider choose “best 21 bunches “
  (~19m)
Includes ~2/3 of captured μ’s
  many are lost
21bunches are recombined to 1 in collider scenario
  It is more difficult to recombine 21 than 12
Would like to extend acceptance or generate shorter train
0m
65m
93m
131m
215m
~ end of rotator
~ After ~80m

## Slide 9: Compare without/with chicane
0 GeV/c
1600 GeV/c
0m (production target)
66m (after chicane/absorber)
88m (after drift)
109m (after buncher)
132m (after rotator)
190m (after cooling)
-30m
50m
0m
57m
79m
102m
152m
1600 GeV/c
0 GeV/c
-30m
-50m
21 bunches for Collider

## Slide 10: Simulation nonresults
NERSC does not work (for me)
Batch Jobs submitted “run” using no time, no output, no useful diagnostics
  has run properly a couple of times
Hidden UNIX system feature?

## Slide 11: Summary
Are studying 325 MHz version (~Collider)
  produces more bunches in same length bunch train than 200 MHz
  requires more bunches to be recombined ~12  21
    more difficult … ?
    HCC recombiner ?
  Are including chicane/absorber
  Would like to fit more μ in fewer bunches

## Slide 12: Weekly Summary