## Slide 1: FRIB Preseparator Radiation Environment and Superconducting Magnet Lifetime Estimates
Roger Roberts, Dali Georgobiani, Reg Ronningen

## Slide 2: Outline
FRIB, Preseparator Scope
Radiation environment
Expectations of magnet life from RIA R&D
Magnet life from present study
  Target + Primary Beam Dump
  Target + Possible Second Beam Dump
Summary and path forward

## Slide 3: FRIB Fragment Separator is within Experimental Systems Project Scope
Facility requirements
  Rare isotope production with primary beams up to 400 kW, 200 MeV/u uranium
  Fast, stopped and reaccelerated beam capability
  Experimental areas and scientific instrumentation for fast, stopped, and reaccelerated beams
Experimental Systems project scope
  Production target facility
  Fragment separator
Experimental areas for fast, stopped, and reaccelerated beams

## Slide 4: Fragment Preseparator Integrated With Target Facility
Target Facility Cutaway View
Cutaway View

## Slide 5: Fragment Separator Layout
Preseparator
  Horizontal Stage
    In “Hot Cell”
  Vertical Stage
    Outside “Hot Cell”
Separator
  Second, Third Stages
    Within Current NSCL
Hot Cell
Target Tank
Dipole/Beam Dump Tank
Wedge Tank
Vertical transfer elements
Hot Cell

## Slide 6: Preseparator and Vacuum Vessels in Hot Cell
Target
SC quadrupoles
Resistive octupole
SC dipoles
Beam dump
North hot cell wall
Steel shield blocks
Beamline from linac
Wedge assembly
Metal shield
HTS quadrupole
Room temperature Multipole
Target
vacuum vessel
Beam dump
vacuum vessel
Wedge
vacuum vessel
meters
SC quadrupoles
Vacuum Isolation Wall

## Slide 7: Target Assembly Requirements
400 kW, 200 MeV/u 238U beam
  Up to 200 kW dissipated
  1 mm diameter
Target speed requirement
  5,000 rpm disk rotation – needed to prevent overheating of carbon disks
Water cooled HX, subject of ongoing design validation efforts
  Allows rapid extraction of heat from beam interaction with target disks
1 mm positioning tolerance
Remotely serviceable/ replaceable from lid
Sufficient space available to accommodate future target designs (incl. liquid metal)
BEAM
Pneumatic Motor
(in 1 atmosphere)
Rotating Air Coupling
Ferro Fluidic Bearing /Seal Assy
Shield Block
Ceramic Bearing
Ø1” Inconel Shaft
Carbon Disk / Heat
Exchanger Assembly
Integral box HX
50 kW prototype target to verify design

## Slide 8: Beam Dump Scope and Technical Requirements
Intercept primary beam
  Well-defined location
  Needs to be adjustable
High power capability up to 325 kW
  High power density: ~ 10 MW/cm3
Efficient replacement
  1 year lifetime desirable
  Remotely maintainable
  Appropriately modular based on remote maintenance frequency
Compatible with fragment separator
  Must meet fit, form, function
Compatible with operating environment
  Vacuum ~10-5 Torr; magnetic field ~ 0.25 T; average radiation levels ~ 104 rad/h (1 MGy/y)
Safe to operate
Range of beam, fragments
Desired fragment
Target
Dipole Magnets
Quadrupole
magnets
Beam Dump Assembly

## Slide 9: Primary Beam Position on Dump Changes with Fragment Selection
Color-code: FBρ is the ratio of the magnetic rigidity of a given fragment to that of the primary beam.
The location of the primary beam at the beam dump is shown with the same color code.
Primary beam trajectory range
Incoming beam direction
Adjustable beam dump position
Fragment beam

## Slide 10: Spatial Distribution of Beam and Fragments on Dump Depends on Fragment Selection
Example: 132Sn fragment distributions for 238U + C fission
Beam and fragments are in close proximity
  5 charge states, most restrictive “spot” sizes σx ≈ 2.3 mm, σy ≈ 0.7 mm
Other beam/fragment combinations will be distributed differently
Drum Dump
Fragment Catcher
Fragment Catcher

## Slide 11: Neutron Production Cross Sections in Heavy Ion Reactions - Example
600 MeV/u Si + Cu
HIMAC (NIRS, Chiba, Japan)
L. Heilbronn, C. J. Zeitlin, Y. Iwata, T. Murakami, H. Iwase, T. Nakamura, T. Nunomiya, H. Sato, H. Yashima, R.M. Ronningen, and K. Ieki, “Secondary neutron-production cross sections from heavy-ion interactions between 230 and 600 MeV/nucleon”, Nucl. Sci. and Eng., 157, pp. 142-158(2007)
For thick-target yields, see:
  T. Kurosawa et al., “Neutron yield from thick C, Al, Cu and Pb targets bombarded by 400 MeV/nucleon Ar, Fe, Xe, and 800 MeV/nucleon Si ions,” Phys. Rev. C, 62, 044615 (2000)

## Slide 12: Study of Soil, Groundwater Activation
400 kW, 637 MeV/u 18O
Beam and Fragments with Z>1
Neutron Flux Density (to 2x1013 n/cm2-s)
Star Density Production Rate in Soil
Soil
Concrete
Steel

## Slide 13: Codes are Benchmarked, Validated for Calculations Critical to Design
Benchmark study performed for 400 kW 433 MeV/u 18O beam
  Upgrade energy
  Energy of beam is at beam dump
Purpose was to benchmark MCNPX (used for target building shield analysis) against MARS15 (used for linac shield analysis)
Problem with MCNPX 2.6.0 – has not been used in analyses when transporting heavy ions - Stepan G. Mashnik, “Validation and Verification of MCNP6 Against Intermediate and High-Energy Experimental Data and Results by Other Codes, International Conference on Mathematics and Computational Methods Applied to Nuclear Science and Engineering (M&C 2011), Rio de Janeiro, RJ, Brazil, May 8-12, 2011.
Model
MARS15
MCNPX2.6.0
MCNPX2.7e
Problem with MCNPX2.6.0
Neutron production cross-sections
for 600 MeV/u Si on Cu

## Slide 14: RIA R&D Work: Model of BNL Magnet Design circa 2006

## Slide 15: RIA R&D Expectations: Coil Life [y]
22C from 350 MeV/u 48Ca + Li
Target | Liquid lithium target |  |  |  |  | Beryllium target |  | 
Projectiles | 48Ca | 48Ca | 86Kr | 136Xe | 238U | 48Ca | 86Kr | 136Xe
Energy | 350 | 500 | 520 | 500 | 400 | 500 | 520 | 500
(MeV/nucleon) |  |  |  |  |  |  |  | 
Q1 | 9 | 5 | 7 | 13 | 33 | 8 | 17 | 29
Q2 | 14 | 3 | 21 | 57 | 132 | 33 | 66 | 113
Q3 | 25 | 8 | 47 | 88 | 198 | 53 | 198 | 264
Dipole | 12 | 5 | 20 | 20 | 396 |  | 264 | 396
Sextupole | 26 | 23 | 19 | 61 | 38 |  |  | 
Q4 | 396 | 113 | 79 | 396 | 198 |  |  | 
Q5 | 1980 | 159 | 264 | 793 | 793 |  |  | 
Q6 | 7930 | 793 | 396 | 3960 | 3960 |  |  | 
Q7 | 7930 | 793 | 793 | 7930 | 7930 |  |  | 
Q8 | 39600 | 2640 | 1980 | 7930 | 7930 |  |  | 
Q9 | 7930 | 7930 | 396 | 2640 | 7930 |  |  | 

## Slide 16: FRIB Baseline Beam Parameters
Beam Parameters
  400 kW on target
  Target extent is 30% of ion range
Baseline Energies
  Upgrade energies ~x2 larger
    Secondary fluxes ~ x4 larger
  Beam current (for 400 kW) ~ x0.5 – smaller
    Expect doses to increase by ~x2
    Angular distributions more forward peaked
Operational Year
  2x107s (5556 h)
Beam Ion | Specific Energy [MeV/u] | Particle Current for 400 kW [ions/s] [x1013] | Target Thickness for ~ 30% of Ion Range [cm]
18O | 266 | 52 | 2.22
48Ca | 239.5 | 22 | 0.79
86Kr | 233 | 12 | 0.43
136Xe | 222 | 8 | 0.29
238U | 203 | 5 | 0.17

## Slide 17: Radiation Heating in Magnets Determined Supports Magnet and Non-conventional Utility Design
Q_D1013
S_D1045
DV_D1064,
DV_D1108
Q_D1137, Q_D1147
Q_D1195, Q_D1207
Two models were used for MCNP6, PHITS calculations of heating in magnets: the large-scale model (left) and a model for the possible second beam dump implementation (above)
Q_D1024
Q_D1035
Q_D1158, Q_D1170
Q_D1218

## Slide 18: Magnet Technologies Assumed
Magnet Technologies Assumed
Expected Lifetime in Units of Radiation Dose [Gy]
Material | Expected Lifetime [Gy]
HTSC | (1 – 2)x108
NbTi | ~5x108
Nb3Sn | ≥5x108
Copper | > 108
Ceramics(Al2O3, MgO, etc) | > 109
Organics | > 106 to 108
Order in Separator | FRIB ID | Magnet Type | Coil Technology
1 | Q1b | Quadrupole | Cu+Stycast
2 | Q2b | Quadrupole | Not yet modeled
3 | Q3b | Quadrupole | Cu+Stycast
4 | Q_D1013 | Quadrupole | HTSC (YBCO)
5 | Q_D1024 | Quadrupole | NbTi+Cu+Cyanate Ester
6 | Q_D1035 | Quadrupole | NbTi+Cu+Cyanate Ester
7 | OCT_D1045 | Octupole-Sextupole | Hollow Tube Cu+MgO
8 | DV_1064 | Dipole | NbTi+Cu+Cyanate Ester
9 | S_D1092 | Octupole-Sextupole | Hollow Tube Cu+MgO
10 | DV_D1108 | Dipole | NbTi+Cu+Cyanate Ester
11 | Q_D1137 | Quadrupole | NbTi+Cu+Cyanate Ester
12 | Q_D1147 | Quadrupole | NbTi+Cu+Cyanate Ester
13 | Q_D1158 | Quadrupole | NbTi+Cu+Cyanate Ester
14 | Q_D1170 | Quadrupole | NbTi+Cu+Cyanate Ester

## Slide 19: Prompt Radiation Maps
400 kW, 550 MeV/u 48Ca
Neutron Flux Density (to 2x1011 n/cm2-s)
Beam and Fragments with Z>1
Preseparator tuned for 42P

## Slide 20: Radiation Heating in Magnets Example: Heating, Quadrupole Cross-section
2D IDL frames of MCNP6 heating mesh tally into Windows Movie Maker
Δx = Δz = 1 cm; Δy = 0.5 cm

## Slide 21: Expected Life of Preseparator Magnets
Iron, W shields studied
  Need to value-engineer shield
  Average heating quoted, maximum values under study and are likely factors of several larger
 | Iron Shield |  |  |  |  | W Shield |  |  |  | 
Projectiles | O18 | Ca48 | Kr86 | Xe136 | U238 | O18 | Ca48 | Kr86 | Xe136 | U238
Energy (Mev/nucleon) | 266 | 239.5 | 233 | 222 | 203 | 266 | 239.5 | 233 | 222 | 203
 | Expected Life [y] |  |  |  |  | Expected Life [y] |  |  |  | 
Q1b (BDS) | 1.7E+04 | 3.3E+04 | 6.3E+04 | 6.9E+04 | 9.0E+04 |  | 1.63E+04 | 2.72E+04 | 4.55E+04 | 4.55E+04
Q2b (BDS) |  |  |  |  |  |  |  |  |  | 
Q3b (BDS) | 3448 | 6784 | 11765 | 14493 | 19011 |  | 3401 | 5675 | 9452 | 5675
Q_D1013 | 2 | 4 | 5 | 68 | 6 |  | 9 | 15 | 32 | 6
Q_D1024 | 149 | 368 | 391 | 481 | 435 |  | 397 | 1323 | 2415 | 2778
Q_D1035 | 66 | 80 | 130 | 495 | 179 |  | 242 | 180 | 120 | 17
OCT_D1045 | 1818 | 1946 | 7364 | 495 | 4630 |  | 7003 | 11820 | 16077 | 14205
DV_1064 | 37 | 28 | 45 | 561 | 36 |  | 28 | 42 | 96 | 35
S_D1092 | 71 | 79 | 5 | 78 | 5 |  | 80 | 7 | 391 | 5
DV_D1108 | 3333 | 3731 | 706 | 867 | 2688 |  | 284 | 370 | 318 | 407
Q_D1137 | 2500 | 13228 | 994 | 2907 | 3067 |  | 2463 | 26178 | 25126 | 8532
Q_D1147 | 1333 | 2404 | 216 | 39 | 6570 |  | 16722 | 16835 | 3086 | 1381
Q_D1158 | 1333 | 7062 | 7645 | 72 | 21930 |  | 92593 | 6196 | 30 | 329
Q_D1170 | 1048 | 30303 | 862 | 110 | 21645 |  | 45045 | 5675 | 12690 | 2841

## Slide 22: Model of Geometry for PHITS Calculation
quadrupole,
transverse view
4 quads before the wall (Q1 to Q4), in Al tank.
3 quads after the wall (Q5 to Q7), in concrete.
Bore diameters: Q1 – 44 cm, others – 40 cm.
Lengths with coils [cm]: 79,84,84,84,76,96,76
beam dump
(water, aluminum)
collimator (Hevimet)
Q1
cast iron
Duratek
Coils (NbTi+Cu+
Stycast or Cyanate Ester)
aperture, collimator (Hevimet)
wedge
dipole
S1
S3
S2
86Kr beams, E = 233 MeV/u
S1,S2,S3: 300,10,0.32 kW

## Slide 23: Geometry for Magnets
Models for PHITS calculations for possible 2nd beam dump operation

## Slide 24: Shielding in Vertical Preseparator Region Sufficient for 2nd Beam Dump Implementation (Worst Case)
Duratek steel at minimum density spec
Concrete walls
Beam dumps
Aperture, Wedge, Collimator
Dipole steel
Radiation plots – results of studies? Assume the are still planned to be included
Residual photon dose rates after 4 hr
Sources: 86Kr beams, 233 MeV/u located at possible second beam dump, fragment catcher, collimator, wedge system
Hands-on access possible in vertical separator region
Concrete bunker around quad triplet reduces prompt dose rate to < 100 mrem/h
Space behind concrete support filled with soil - within building: Activated soil is contained

## Slide 25: Radially Averaged Dose Rates To Quadrupoles
Model coils contain Stycast
Model coils contain NbTi(75%)+Cu(25%)

## Slide 26: Radiation Heating in Magnets Example: Heating, Quadrupole Cross-section
2D IDL frames of PHITS heat mesh tally into Windows Movie Maker
Δx = Δz = 1 cm; Δy = 1 cm

## Slide 27: Radiation Heating in Magnet Yokes, Coils Supports Magnet and Non-conventional Utility Design
Magnets | Yoke Heating [W]
Q_D1137 | 52
Q_D1147 | 22
Q_D1158 | 11
Q_D1170 | 9
Q_D1195 | 3
Q_D1207 | 4
Q_D1218 | 2
86Kr, 233 MeV/u, at 300 kW
Magnets | Coil Dose Rate [MGy/y] | Lifetime [y]
Q_D1137 | 2.54 | 10
Q_D1147 | 0.87 | 29
Q_D1158 | 0.80 | 32
Q_D1170 | 0.56 | 44
Q_D1195 | 0.14 | 182
Q_D1207 | 0.05 | 497
Q_D1218 | 0.04 | 673

## Slide 28: Summary
FRIB radiation environment is challenging
  Power
  Wide range of beams, beam trajectories
  Shield studies are important
SC technology will work