Front End 5.1
- Added IDS120k target
- Realistic target aperture
- Realistic coil geometries
- Added RF windows back into RF capture region
  - Same as old windows
- Old beam file (would it change?)
- Still anomalous low G4BL throughput
  - Not tried to tidy this up

---
Capture/Drift
Capture/Drift (G4BL)
4000
mm
9929
mm
15000
mm
41000 mm
100
mm
800 mm
800
mm
1046 mm
1046 mm
600 mm
600 mm
12.5o
Kill
Lithium Hydride
Beryllium
Capture/Drift (ICOOL)
4000
mm
9929
mm
15000
mm
41000 mm
100
mm
800
mm
1046 mm
600 mm
12.5o
600 mm
Kill
Lithium Hydride
Beryllium
r^{2} = {(r_{1}^{2} - r_{0}^{2})z} over {z_{1}} + r_{0}^{2}
In target region fields are defined by a coil set
Beampipe radius in target area follows
with
R0 = 75 mm
r1 = 300 mm
z1 = 15000 mm
In G4BL this is implemented as a volume of
rotation with rotation surface found by linear
interpolation off grid points every 5 mm in r. In
ICOOL a series of cylinders are used with inner
edge every ~ 5 mm in r.
The chicane consists of a bend and reverse
bend through 12.5o with radius of curvature
22917 mm to the centre of the beam pipe.
In ICOOL this is simulated using an idealised
Bs ~ 1/r; in G4BL this is simulated using coils
arranged periodically on the toroid.
Note due to the “cartoon” nature of the
schematic the transverse displacement in the
chicane looks deceptively small – it is in fact a
little more than 1 beam pipe diameter.
G4BL chicane coils have:
Inner radius: 430 mm
Outer radius: 530 mm
Length: 180 mm
Current Density: 16.57 A/mm2
Placed at 0.625o intervals (250 mm in s)
From the end of the chicane onwards both
lattices use constant 1.5 T field

---
Coil designation	Units	1	2	3	4	5	6	7
Current density	kA/cm2	2.20	2.07	1.41	1.20	1.06	1.93	2.18
Coil length	cm	100.18	123.64	207.15	212.02	215.63	352.32	77.78
Upstream end	cm	-87.56	-111.03	-120.98	-125.85	-129.46	-240.93	111.39
Downstream end	cm	12.62	12.61	86.17	86.17	86.17	111.39	189.17
Inner radius	cm	18.34	23.85	29.58	36.21	43.30	120.00	120.00
Outer radius	cm	23.10	28.76	35.52	42.64	50.16	195.83	184.34
Coil designation	Units	8	9	10	11	12	13	14
Current density	kA/cm2	2.67	3.35	4.12	4.07	4.50	4.67	4.64
Coil length	cm	45.20	31.23	255.37	15.45	13.00	341.31	10.96
Upstream end	cm	276.47	470.24	575.75	914.32	1034.76	1085.07	1454.28
Downstream end	cm	321.67	501.46	831.12	929.76	1047.76	1426.38	1465.24
Inner radius	cm	120.00	119.96	89.65	118.28	72.36	69.92	69.94
Outer radius	cm	195.83	175.59	93.81	170.31	86.91	72.38	86.39
G4BL uses coil designations 1 through 14; beyond coil 14 a series of match coils are used with following parameters to match into chicane
Centre z [mm]	J scale	Centre z [mm]	J scale
15000	0.90	17000	0.97
15250	0.80	17250	0.97
15500	0.80	17500	0.97
15750	0.90	17750	0.97
16000	0.95	18000	1.00
16250	0.95	18250	1.00
16500	0.95	18500	1.00
16750	0.95	18750	1.00
Match coil current: 16.57*(J scale) A/mm2
Match coil inner radius: 430 mm
Match coil outer radius: 530 mm
Match coil length: 180 mm

---
Coil designation	Units	15	16	17	18	19	20
Current density	kA/cm2	4.64	4.64	4.64	4.64	4.64	4.64
Coil length	cm	14.12	320.34	14.12	14.12	320.34	14.12
Upstream end	cm	1536.00	1589.83	1949.88	2036.00	2089.83	2449.88
Downstream end	cm	1550.12	1910.17	1964.00	2050.12	2410.17	2464.00
Inner radius	cm	71.88	50.08	71.88	71.88	50.08	71.88
Outer radius	cm	90.00	52.42	90.00	90.00	52.42	90.00
ICOOL uses the full coil pack 1 through 20 to generate a field map but only in the region up to 15000 mm.
Beyond 15000 mm a constant 1.5 T field is used. Fields are generated from 5 current sheets spaced equally
across the coil area.

---
RF Capture
Capture Cell (G4BL)
Field is constant 1.5 T (no coils simulated)
Window thickness dt in buncher: 0.2 mm
Window thickness dt in phase rotation: 0.4 mm
“Buncher” refers to variable voltage section
“Phase rotation” refers to fixed voltage section
5 mm
500 mm
600 mm
750 mm
dt
Kill
Lithium Hydride
Beryllium
500
mm
Capture Cell (ICOOL)
dt
dt
600 mm
Kill
750 mm
Lithium Hydride
Beryllium

---
Capture Performance (400k pot)

---
Capture Performance (400k pot)

---
Plan towards new baseline
From IDS #9
Implement new coil/cooler geometry in current deck (Diktys)
  - Make a “release” of the lattice files
  - Use as basis for cooling channel selection
Implement G4BL version of chicane/proton absorber/RF capture (Rogers)
  - Use with ICOOL deck as basis for documentation of the chicane/proton absorber
  - Using current baseline (i.e. not including engineering modifications)
Merge chicane etc into the new coil/cooler geometry
  - Make a “release” of the lattice files
Merge new target
  - Make a “release” of the lattice files
- Not happy with anomalously low G4BL capture results – needs study