## Slide 1: transport Study for The Muon Collider/Neutrino Factory Frontend
HISHAM KAMAL SAYED
Physics Department
BROOKHAVEN NATIONAL LABORATORY
TGT-AAG Meeting Dec. 13th 2012

## Slide 2: Baseline Optimized Parameters (X. Ding)
Hg Target
  θTarget=0.137 rad
  RTarget=0.404 cm
Proton Beam
  E=8 GeV
  θBeam=0.117 rad
  σx=σy=0.1212 cm (Gaussian Distribution)
  σt=σz=0 (Pancake Distribution)
Solenoid Field
  IDS120h  20 T peak field at target position (Z=-37.5)
  Aperture at Target R=7.5 cm - End aperture R = 30 cm
  Fixed Field Z = 15 m  Bz=1.5 T

## Slide 3: Analytic form for Tapered Solenoid
Inverse-Cubic Taper
Field at R=0
Off-axis field approximation
! First Order
BZ = B1 / CUBIC**POW
BR = -R / 2. * DBZ1
! Second Order
BZ = BZ - R**2 / 4. * DBZ2
BR = BR + R**3 / 16. * DBZ3
! Third Order
BZ = BZ + R**4 / 64.0 * DBZ4
BR = BR - R**5 / 384.0 * DBZ5
! Fourth Order
BZ = BZ - R**6 / 2304.0 * DBZ6
BR = BR + R**7 / 18432.0 * DBZ7

## Slide 4: Initial Particle Distributions
Distribution of all Mesons at z=0
Distribution of Muons which made it to the end of cooling section and satisfied acceleration acceptance cuts

## Slide 5: Good Muons Particle Distributions
Distribution of Muons which made it to the end of cooling section and satisfied acceleration acceptance cuts
Distribution of all Mesons at z=0

## Slide 6: Mesons Initial Distribiution

## Slide 7: Fixing time of arrival
TOA Protons at z=-200 cm
TOA Protons at z=-75 cm
MARS simulation was performed with a “pancake” shaped proton beam, lunched at t=0 from a specified z<0.
The Gaussian time distribution is “usually” produced by using a random Gaussian generator on the meson distribution at z=0.

## Slide 8: Transmission
MARS simulation results:
Counting muons at 50 m with K.E. 80-140 MeV
Solenoid Taper Length [cm]

## Slide 9: Transmission
Nmuons{Good}
Nmuons{Pz cut}
Nmuons{All cuts}
Good particles are those who satisfy the following conditions/cuts
Survived the phase rotator and cooling sections
Acceleration acceptance cuts
  0.1 <Pz< 0.3 GeV
  Transverse cut R < 0.3 m
  Longitudinal cut < 0.15 m

## Slide 10: More Cooling
Baseline cooling end
140 cell (z=265 m)
For every taper length optimized TOA
For 8 m taper length TOA scan

## Slide 11: Time & Taper Length scan
Using baseline cooling section
(140 cooling cell)
Using longer cooling section
(200 Cooling cell)

## Slide 12: Time & Taper Length scan
TOA for optimum throughput at end of cooling for each capture solenoid case

## Slide 13: Phase Space Distributions

## Slide 14: Phase Space Distributions

## Slide 15: Phase Space Distributions

## Slide 16: Phase Space Distributions

## Slide 17: Phase Space Distributions

## Slide 18: Phase Space Distributions

## Slide 19: Phase Space Distributions

## Slide 20: Phase Space Distributions (Short versus long taper)
Pions

## Slide 21: Phase Space Distributions (Short versus long taper)
Pions

## Slide 22: Phase Space Distributions (Short versus long taper)

## Slide 23: Phase Space Distributions (Short versus long taper)

## Slide 24: Conclusion & Summary
Longer tapers have more meson yield at the decay channel (z=50).
Shorter tapers produce “more good” muons which could be bunched & cooled.
The maximum yield requires tapers with z=4-6 m.
Adding longer cooling channel is required to reach maximum cooling.