## Slide 1: 2D Jet Simulation Updates
Jan.23rd 2014
Yan Zhan
SUNY Stony Brook

## Slide 2: Problem 1: Water-Air Jet
An axis-symmetric water jet into still air with a mean bulk velocity of 4.5455 m/s (D = 0.01m, and Re = 50,000).

## Slide 3: Boundary Conditions
Outflow

## Slide 4: Jet Characteristics
Physical Characteristics
Numerical Characteristics
  Determination of the mesh size:
Assume only primary breakup, the critical liquid Weber number is 10, then Δx_critical = 34.4μm
Diameter (D) | Velocity | Turbulent Intensity
0.0102108 m | 4.5455 m/s | u‘/U = 0.05
m
Phase | Density | Viscosity | Surface Tension
Air | 1.225 kg/m3 | 1.46×10-5 m2/s | 0.071 N/m
Water | 998 kg/m3 | 0.9×10-6 m2/s | 
Notes: Jet primary breakup: Drop formation along the surface of jet.

## Slide 5: Mesh
Halved (axis-symmetric) model with grid# of 822,000

## Slide 6: Results (t = 0.0307s)

## Slide 7: Problem 2: Menard’s Test[1]
[1] T. Menard, etc., Coupling level set/VOF/ghost fluid methods: Validation and application to 3D simulation of the primary break-up of a liquid jet, International Journal of Multiphase Flow 33 (2007) 510–524
50D
20D
An axis-symmetric liquid jet into still gas with a mean bulk
velocity of 100 m/s (D = 100 μm, and Re = 5,800).

## Slide 8: Menard’s Results[1]
Jet development and penetration (dt = 2.5 μm)

## Slide 9: Boundary Condition
50D
20D
Outflow

## Slide 10: Jet Characteristics
Physical Characteristics
Numerical Characteristics
  Determination of the mesh size:
Assume only primary breakup, the critical liquid Weber number is 10, then Δx_critical = 2.36 μm
Diameter (D) | Velocity | Turbulent Intensity
100 μm | 100 m/s | u‘/U = 0.05
m
Phase | Density | Viscosity | Surface Tension
Gas | 25 kg/m3 | 4x10-7 m2/s | 0.06 N/m
Liquid | 696 kg/m3 | 1.724×10-6 m2/s | 

## Slide 11: Mesh
Halved (axis-symmetric) model with grid# of 1,146,880

## Slide 12: Results
Set Up 1 (t = 0 s):

## Slide 13: Results
Set Up 1 (t = 10 μs):

## Slide 14: Results
Set Up 1 (t = 30 μs):

## Slide 15: Results
Set Up 2 (iteration = 0 ):

## Slide 16: Results
Set Up 2 (iteration = 1500 ): :

## Slide 17: Results
Set Up 2 (iteration = 3500) :

## Slide 18: Results
Set Up 2 (iteration = 4500) :
Next:
Turn to Unsteady Simulation

## Slide 19: More Information
[2] P-K Wu and G M Faeth, Onset and end of drop formation along the surface of turbulent liquid jets in still gases, Phys. Fluids, Vol. 7, No. 11, November 1995
Surface breakup regime map for turbulent liquid jets in still gases when aerodynamic effects are small (liquid/gas density ratios are larger than 500)[2]
Considered Range:
Weber numbers (
1.0X 102- 1.1X1 06;
Reynolds numbers () : 3.4X103-8.5X 105 ;
Ohnesorge numbers () : 0.001-0.017.

## Slide 20: More Information
Problem # |  |  |  |  | 
Problem 1 | 2,904 | 50,000 | 0.001 | 9.568d | 10.387d
Problem 2 | 11,600 | 5,800 | 0.01857 | 3.783d | 106.4d
Problem # |  |  |  |  | 
Problem 1 | 2,904 | 50,000 | 0.001 | 9.568d | 10.387d
Problem 2 | 11,600 | 5,800 | 0.01857 | 3.783d | 106.4d