## Slide 1: Neutrino Factory Target Cryostat Review
Van Graves
Cale Caldwell
IDS-NF Phone Meeting
August 10, 2010

## Slide 2: General Target Concept – Downstream Mercury Drain
Iron
Plug
Proton
Beam
Nozzle
Tube
SC-1
SC-2
SC-3
SC-4
SC-5
Window
Mercury
Drains
Mercury
Pool
Water-cooled
Tungsten Shield
Mercury
Jet
Resistive
Magnets
Neutrino Factory Study 2 Target Concept
ORNL/VG
Mar2009
Splash
Mitigator

## Slide 3: General Target Concept – Upstream Mercury Drain

## Slide 4: NF Cryostat with Tapered Shielding
Taper matches capture field
No shielding under mercury
Straight W-C bore up to beam window to allow removal of mercury chamber

## Slide 5: Tapered Shielding Concept Dimensions

## Slide 6: Cryostat Modules
All insertion/extraction from upstream end
Locating & supporting features not shown – will require additional space

## Slide 7: Cryostat Modules Full View
Module weight supported by cryostat? Probably not – another structure required
Remote handling of these modules not trivial
Note slot in shielding module for mercury chamber

## Slide 8: Assembled Cryostat
Resistive magnet leads & water cooling for these modules also enter from upstream

## Slide 9: Original: 5cm Shielding at SC1

## Slide 10: V2: 10cm Shielding Below Resistive Magnets, 15cm Above
Allows mercury drainage below magnets while still providing W-C shielding

## Slide 11: V2 Iso: 10cm Shielding Below Resistive Magnets, 15cm Above
Asymmetric W-C structure, minimal shielding for SC1

## Slide 12: V3: 30cm Shielding Below, 35cm Above, Constant ID

## Slide 13: V3 Iso: 30cm Shielding Below, 35cm Above, Constant ID
Simpler W-C shielding fabrication, sized to protect SC1

## Slide 14: Some Questions as Design Progresses
Can system perform without iron plug and/or resistive magnets?
  Removal simplifies remote maintenance, provides more space for nozzle & beam dump.
What does internal cryostat structure (weight support, magnet force restraints) look like, and how does it affect overall cryostat size?
Are 5 SC magnets required in this cryostat?
  Downstream beam window should be at end of cryostat for remote maintenance from downstream end.
What shielding thickness is required to protect SC1?
  This will ultimately drive cryostat bore diameter.

## Slide 15: Summary & Reminders
Current NF target design based on physics performance characteristics
Further consideration shows it is an assembly of several subsystems, each with different design requirements and trade-offs
  Several areas of engineering-related R&D, including heat removal, Hg flow, nozzle development, beam windows
With Hg target (nor with any other target), hands-on maintenance cannot be assumed at any point in operation
  Remote features must be incorporated into initial design
Final system concept will result from an integrated design approach with input from several technical areas