## Slide 1: Shield Module Design Considerations
Adam Carroll
Van Graves
July 3, 2014

## Slide 2: Overview
Capability to remotely remove and reinstall the shield modules is required
Shield module concept is He-cooled tungsten spheres
Current shield modules weigh up to 200 tons
Cradle needs to be sized to support shielding
Tungsten Shielding
SC1
Cradle
SC2

## Slide 3: 20to2T5m120cm4pDL Shielding Module Volumes
1
2
3
4
5
6
Module | Volume (m^3) | Weight (MT)* | Weight (ton)
1 | 13.16 | 152.0 | 167.6
2 | 0.89 | 10.3 | 11.9
3 | 7.45 | 86.0 | 95.0
4 | 20.57 | 237.6 | 262.0
5 | 11.75 | 135.7 | 150.0
6 | 12.61 | 145.6 | 160.5
*Assuming density of 19,250 kg/m^3, packing factor of 60%

## Slide 4: Shield Supports
Current concept is simple stand integrated with cryostat
Provides curved shelf to support shield weight without transferring load to cryostat
Mounted to base platform that can be moved laterally out of beam line
Some design considerations
  Inter-coil forces
  Shielding module support & removal
  Stability under weight
  Space requirements
  Shorter preferred in height and along beam axis
Leg footprint: 100mm X 1600mm
Shelf thickness: 40mm

## Slide 5: Translating the shielding
Shielding
Options for shield module extraction
  Sliding material, low friction material to reduce force required to drag shielding
    Best materials not radiation tolerant
    Steel on steel: µs = 0.5 – 0.8
    Steel on brass: µs = 0.35
  Tracked wheels, removes significant shielding space, difficult due to high weights, may be possible
  Rollers, removes significant shielding space, but rad-hard and reliable
  Lubricants likely not allowed
Rollers considered for this presentation

## Slide 6: Shielding Cut Away for Roller
31 cm
60 cm
Shielding cutaway required to allow space for rollers
Potentially could be optimized to provide more shielding, but a significant localized shielding reduction will always be required

## Slide 7: Rollers
Hilman Rollers
High weight capacity required
  First concept is commercially available hardware with adequate capacity
Minimum of three pairs required
Continuous line of rollers reduces stress on cradle (see two slides forward for comparison)

## Slide 8: Cradle Stress
Initial cradle design with the addition of a track is insufficient to support the weight of the shield.
Transforming the cradle into a tube significantly improves its strength.

## Slide 9: Cradle Stress
Max Stress ~15ksi
Max Stress above yield
Continuous rollers produce lower stress on cradle
Other potential worse case loading situation may occur as the shield module is extracted, those situations will need to be considered to continue the conceptual design
Three Pair
Continuous
Note: images don’t use same scale

## Slide 10: Cradle Buckling
Buckling of the cradle was analyzed
~55x load factor calculated
  Buckling not a concern in current concept
Horizontal forces from inter-coil attraction/repulsion not considered

## Slide 11: Conclusions
Remotely handling the shielding modules is a significant challenge
Rollers are an option, optimization to reduce shielding loss required
Cradle requires some strengthening to handle the shielding load
Extraction procedure and tooling concepts need to be developed
Smaller shielding modules beneficial from remote handling perspective
  One shield per coil, one coil per cryostat
  Cryostat performance must be considered
  More utility connections required
  Increases number of inter-coil forces if each coil is in its own cryostat
  More and/or larger gaps between cryostats