## Slide 1
The Front End

## Slide 2: Outline
Define Front End
Major Sub-systems
Key Challenges
Future R&D Activities

## Slide 3: The Muon Collider/Neutrino Factory Front End
The Front End is that portion of the facility following the proton driver and target which delivers muons to the Muon Collider 6d cooling system or the Neutrino Factory acceleration system.
The proton source will have different bunch structures.
Neutrino Factory
(with 4D cooler)
Muon Collider
(no 4D Cooler)

## Slide 4: The Major Front End Sub-Systems
Drift/Decay Channel (π→μ)
Buncher
Rotator
4D Cooler
18.2 m
~65m
FE Target
Solenoid
Drift
Buncher
Rotator
Cooler
~33m
~42 m
~75 m
p
π→μ
Target
Front End

## Slide 5: Key Buncher/Rotator Parameters
Buncher
37 rf cavities
320 to 233.6 MHz (13 frequencies)
7.5 MV/m Peak rf gradient
24 MW Peak rf power (MC: 0.12 MW avg)
1.5T Peak magnetic field
33 m total length
Rotator
56 rf cavities
230 to 202.3 MHz (15 frequencies)
12 MV/m Peak rf gradient
140 MW Peak rf power (MC: 0.7 MW avg)
1.5 T Peak magnetic field
42 m total length

## Slide 6: The Buncher/Rotator
Pion/Muon Kinetic Energy
cτau
Drift
Buncher
Rotator
Target

## Slide 7: The Cooler
100 rf cavities
201.25 MHz
15 MV/m peak rf gradient
400 MW peak rf power (NF: 8 MW avg)
2.8T peak magnetic field

## Slide 8: Front End Challenges
Buncher/Rotator/Cooler
Shielding of beam line components
Performance of rf cavities in magnetic field
Engineering constraints

## Slide 9: Front End Challenges- Beamline Shielding
Mitigation Strategies
Upstream bent solenoid
Beryllium “beam stop” plugs
J.C. Gallardo
Buncher
Rotator
Cooler
Buncher
Rotator
Cooler

## Slide 10: Bent Solenoid Chicane
10m
P. Snopok
2 X 12.5o
L = 10m

## Slide 11: Proton Removal
Blue: Removed by the chicane Green: Removed by absorber Red: Survive
Proton beam power reduced by 99%
Stacked plot of protons entering into the Chicane

## Slide 12: Muons through the Chicane
μ+
μ-
Muon Front End throughput reduced by 10-15%

## Slide 13: Engineering challenges
IFD-NF Engineering studies:
  Increase the gap between coils in buncher & rotator
  Increase cooler cell length from 75 cm to 86 cm
  Have one “empty” cell after a series of cavities
N. Bliss, IDS-NF Meeting (April, 2012)
Cooler
Rotator

## Slide 14: Increasing the cell length
Simulations show that it is safe to increase the cooler cell to 86cm without loss of performance.
Beyond that point, performance is reduced
D. Stratakis
Acceptance plot
εT = 30mm
εL = 150mm

## Slide 15: Adding a gap between cavities
Group of 3
There is a loss of ~5% if empty cell is after 5 or more cavities. Loss is ~12% for groups of 3
D. Stratakis

## Slide 16: Front End Challenges- RF
Machine performance reduced
μ/p ratio reduced with rf gradient limitations
Mitigation Strategies:
Beryllium walled cavities
Bucked Coil Lattices
High Pressure (GH2 filled) rf cavities
D. Neuffer
30% performance loss with
factor 2 gradient reduction

## Slide 17: Bucked Coils
Axial field reduced at rf cavity walls

## Slide 18: Bucked Coils for the Cooler
Radial BC (RBC)
Baseline
A. Alekou

## Slide 19: ICOOL Simulations
Similar results for both LBC and RBC schemes
20% less muon per protons compared to baseline
BUNCHER
ROTATOR
COOLER

## Slide 20: High Pressure Gas RF
J.C. Gallardo
M. Zisman
Simulation considers:
34 atms GH2
LiH absorbers
Be Isolation windows
15 MV/m rf gradients
εT Red: Vacuum rf Black: HPRF Downstream Acceptance
8% Reduction

## Slide 21: Target Taper
H. Sayed
If Target system goes from 20T to 15T peak field then end field goes from 1.5 T to 1.8T in order to maintain performance

## Slide 22: FY 13 R&D Activities
Integrate Chicane into Decay region
Respond to new Target taper 15T1.8T
  Set Decay channel, Buncher, Rotator to 1.8T
  Establish new matching section into Cooler
  Re-optimize Front End parameters
  Evaluate Front End performance levels
Support IDS-NF RDR activities

## Slide 23: FY 14 & 15 R&D Activities
Optimize Front End for Muon Collider
Respond to rf cavity technology results
Support MAPFP1 activities

## Slide 24: Summary
A Front End baseline has been established
Optimization studies have resulted in a 0.08 μ/p throughput ratio for 8 GeV incoming protons
Key Front End challenges
  Performance of rf cavities in magnetic field
  Energy deposition along Front End channel
Mitigation strategies have been developed to address these challenges