## Slide 1: The High-Power-Target System of a Muon Collider or Neutrino Factory
K. McDonald
Princeton U.
(August 29, 2014)
NuFact’14
U Glasgow

## Slide 2
The Target System Concept
A Muon Collider needs muon beams of both signs.
A Neutrino Factory based on neutrinos from muon decay could operate with only one sign of muons at a time, but advantageous to have both signs.
Could use two proton beams + 2 targets in solenoid horn (as per “conventional” neutrino beams from pion decay).
Or, could use one proton beam + solenoid capture system.
Fernow et al. reviewed options in March 1995,
http://puhep1.princeton.edu/~mcdonald/examples/accel/fernow_aipcp_352_134_95.pdf
Li lenses, plasma lenses, toroidal horns, and solenoidal capture.
All of the pulsed, toroidal systems would be well beyond present technology (then and now!), so the solenoid capture system began to be favored.

## Slide 3
R.B. Palmer (BNL, 1994) proposed a 20-T solenoidal capture system.
Low-energy 's collected from side of long, thin cylindrical target.
Solenoid coils can be some distance from proton beam.
 10-year life against radiation damage at 4 MW.
Liquid mercury jet target replaced every pulse.
Proton beam readily tilted with respect to magnetic axis.
 Beam dump (mercury pool) out of the way of secondary 's and 's.
Target and Capture Topology: Solenoid
Desire  1014 /s from  1015 p/s ( 4 MW proton beam)
IDS-NF Target Concept:
Shielding of the superconducting magnets from radiation is a major issue.
Magnetic stored energy ~ 3 GJ!
Superconducting magnets
Resistive magnets
Proton beam and
Mercury jet
Be window
Tungsten beads,
He gas cooled
Mercury collection pool
With splash mitigator
5-T copper magnet insert; 15-T Nb3Sn coil + 5-T NbTi outsert.
Desirable to replace the copper magnet by a 20-T HTC insert (or 15-T Nb coil).

## Slide 4
Preliminary Costing of a 4-MW Target System
The nominal target costs only a few % of the Target System.
Infrastructure costs are ~ 50%.
(A. Kurup, International Design Study for a Neutrino Factory)

## Slide 5
Liquid or Solid Target?
Muon Colliders/Neutrino Factories favor initial capture of low-energy muon (which are later accelerated to a desirable energy).
The yield of soft pions/muons is higher for a high-Z target.
Solid metal targets would melt in a MW proton beam, unless replaced ~ every beam pulse.
Consider high-Z liquid metal target (He, Pb-Bi, Ga, …) or carbon target.
Studies have alternated between these two options.
Recent effort has emphasized carbon target options.

## Slide 6
Specifications from the Muon Accelerator Staging Scenario
6.75 GeV (kinetic energy) proton beam with 3 ns (rms) pulse.
1 MW initial beam power, upgradable to 2 MW (perhaps even to 4 MW).
60 Hz initial rep rate for Neutrino Factory;
15 Hz rep rate for later Muon Collider.
The goal is to deliver a maximum number of soft muons,
~ 40 < KE < ~ 180 MeV.

## Slide 7
Stainless-steel target vessel (double-walled with intramural He-gas flow for cooling) with graphite target and beam dump, and downstream Be window.
This vessel would be replaced every few months at 1 MW beam power.
15 T superconducting coil outsert,
Stored energy ~ 3 GJ, ~ 100 tons
5 T copper-coil insert. Water-cooled,
MgO insulated
He-gas cooled W-bead shielding (~ 100 tons)
Proton beam tube
Upstream proton beam window
Target System Concept
Last
Final-Focus
quad

## Slide 8
Target System Optimization
for fixed geometric, rms transverse emittance of 5 m

## Slide 9
Target System Optimizations
High-Z favored.
Optima for graphite target: length = 80 cm,
radius ~ 8 mm (with σr = 2 mm (rms) beam radius),
tilt angle = 65 mrad,
nominal geometric rms emittance ε = 5 µm.
β* = σr2 /ε = 0.8 m.
Graphite proton beam dump, 120 cm long, 24 mm radius to intercept most of the (diverging) unscattered proton beam.
The 20 T field on target should drop to the ~ 2 T field in the rest of the Front End over ~ 5 m.
However, difficult to deliver a beam of 5 m emittance with over
1 MW power.

## Slide 10
We prefer target radius  8 mm (beam radius  2 mm) for viable radiation cooling of the target.
For rtarget = 8 mm, same yield for any emittance  20 m.
Yield for 50 m emittance and target radius of 1.2 cm is only 10% less than that for the nominal case of 5 m emittance an 0.8 cm target radius.
Target System Optimization
for variable geometric, rms transverse emittance
No tilt of beam/target
65 mrad tilt of beam/target
Little loss of muon yield for 20 m emittance,
 Can use single beam @ 4 MW.

## Slide 11
Future Target Studies
Muon Collider/Neutrino Factory studies in the USA being ramped down.
Interest remains in high-power targetry for various applications.
  See, for example, the 5th High Power Targetry Workshop (FNAL, 2014),
  https://indico.fnal.gov/conferenceDisplay.py?ovw=True&confId=7870
  [These workshops were initiated by H. Kirk.]
A particular issue: how much beam power can a graphite target stand?
Lifetime against radiation damage much better at high temperature.
Resistance to “thermal shock” from pulsed beams also better at high temperature.
Firm up these trends with data from beam irradiations of high-temperature graphite. (The Muon Collider/Neutrino Factory group participated in beam irradiations of water-cooled graphite and many other target materials in 2002-2006.)
GARD proposal(s) being generated by BNL and FNAL for such studies.
New diagnostic: x-ray diffraction of irradiated samples.