## Slide 1
In the staging scenarios, we consider various proton beam energies and beam powers.
We have come to desire particle production rates quoted in a manner that scale simply with beam power.
Beam Power = Protons/s  Beam Energy;
So, if we are interested in, say, “useful” muons per beam power, this is equivalent to
(“useful” muons/s) / (proton/s) / beam energy.
In the following we abbreviate this to
Muons / proton / GeV
How to Compare Particle Production at Different Beam Energies
Modeling Pion Production at 3 GeV

## Slide 2
Soft-Pion-Production Modeling Issues
MARS15 simulation (X. Ding) with 3 GeV protons and C target shows large production of soft pions (and 2nd peak at 300 MeV KE). Are these features real?
3 GeV
MARS
Au: Pi-
5MPOT
MARS15 simulation (C. Yoshikawa) shows peak of backward - with P ~ 120 MeV/c independent of angle.
MARS15 model of invariant cross section does not seem to have the required drop-off at low KE (from symmetry of the production cross sections with Pz in the center of mass frame). From Mokhov (1012):
http://accelconf.web.cern.ch/accelconf/HB2012/talks/weo3c05_talk.pdf
p + Pb
Collisions plotted vs. KE
Pb + Pb
collisions plotted vs. rapidity y
http://iopscience.iop.org/1367-2630/5/1/301/fulltext/

## Slide 3
LAQGSM Mode  Better MARS Model below 5 GeV
Hg, 8 GeV
C, 3 GeV, in LAQGSM MODE
C, 3 GeV, not in LAQGSM Mode
Hg, 3 GeV
Pion production @ 3 GeV via MARS in LAQGSM mode seems much more plausible than when not in this mode.
As reported previously, pion production off Hg target is lower at 3 GeV than at 8 GeV by almost a factor of 2.
Pion production off C target at 3 GeV is about ¾ that off Hg target at 8 GeV, but greater than that off Hg at 3 GeV.
Pion production off C target at 3 GeV and 1 MW is about 1/5 that off Hg at 8 GeV and 4 MW.
X. Ding: http://puhep1.princeton.edu/~kirkmcd/mumu/target/Ding/ding_130905.pdf

## Slide 4
MARS in LAQGSM Mode Agrees Well with FLUKA @ 3 GeV

## Slide 5
Summary
Models of particle production below 5 GeV are delicate, but MARS in LAQGSM Mode seems robust enough for us to proceed.
At 3 GeV, a carbon target is favored over a mercury one in terms of rate alone (and a carbon target is very viable in a 1 MW beam).
Pion/muon production at 3 GeV, 1 MW with a carbon target will be about 1/5 that with a mercury target at 8 GeV and 4 MW.
Delivering a short pulse in a single proton beam will be difficult at 3 GeV, so we may need to consider multiple beams (onto a single target).
Optimization for the configuration of carbon target, capture solenoid magnets, and possible multiple proton beams should begin now.